Characterization of the Fisher and Carpenter Creek Watershed of Skagit and Snohomish Counties, Washington

Prepared Pursuant to Washington Department of Ecology Centennial Clean Water Fund Grant No. G0400195

“Fisher/Carpenter TMDL Implementation”

Skagit Conservation District

2007

Table of Contents

1	Introduction	3

1.1	Location of the Study Area	3

1.2	Policy Background	3

1.3	Purpose of the Study	3

2	Watershed Delineation	4

2.1	Boundaries	4

2.2	Topography	4

3	Land Use	7

3.1	Relevant Historical Land Use	7

3.2	Existing Land Use/Zoning	7

4	Soils	12

4.1	Soils Description	12

5	Geohydrology	15

5.1	Aquifer	15

6     Surface Water Hydrology	17

6.1	Description of Sub-basins	17

6.2	Impervious Surfaces	22

6.3	Flow	24

6.4	Channel Morphology	25

Wetlands	30

6.6	Key Hydrologic Structures and Fish Passage Blockages	32

7	Water Quality	32

Water Quality Standards	33

7.2 	SCD’s In-House Water Quality Monitoring Program	33

7.3	SCD’s Stream Team Citizen Water Quality Monitoring	36

7.4	Sources of Water Quality Degradation	36

7.5	Quality Assurance / Quality Control	40

8	Fish and Wildlife Habitat	43

8.1	Species Inventory	43

8.2	Evaluation of Habitat Quality	44

8.3	Endangered Species Act	45

Appendices	49

# 1	Introduction

## 1.1	Location of the Study Area

The Fisher/Carpenter Creek Watershed is located in southwest Skagit County and northwest Snohomish County, Washington.  The watershed’s several upland tributaries, manmade drainage channels, and natural slough drain an area of approximately 25.5 square miles, located between the communities of Mount Vernon and Stanwood, Washington.

## 1.2	Policy Background

Section 319 of the Federal Clean Water Act requires states to identify water bodies, which, without control of non-point source pollution, cannot attain applicable water quality standards.  In response to this Federal mandate, the Washington Department of Ecology funded local initiatives to identify and rank such water bodies and to develop action plans for addressing non-point source pollution.

A related provision of the Federal Clean Water Act, Section 303(d), requires states to identify water bodies that do not attain the relevant water quality standards.  Further, states must develop plans for limiting the total point source and non-point source pollution discharges to such water bodies, in order that water quality standards can be attained.  Fisher/Carpenter is identified in Department of Ecology’s 1998, 303(d) listings as a water body that, without control of pollution, cannot attain the State of Washington Water Quality Criteria for temperature and fecal coliform bacteria (Department of Ecology 1998).  Department of Ecology’s revised 303(d) listing includes dissolved oxygen and fecal coliform (Department of Ecology 2004).  The Department of Ecology has not formulated a plan for regulating “total maximum daily loads” of pollution in Fisher/Carpenter Creek to meet State water quality parameters (i.e., temperature, dissolved oxygen and fecal coliform).  This characterization will define and describe in detail the physical and political characteristics of the Fisher/Carpenter Watershed.  It will provide the base for development of a plan that will address and regulate total maximum daily loads of pollution in the watershed.

## 1.3	Purpose of the Study

The goal of this project is to protect, restore, and enhance the water quality, quantity, and fish and wildlife beneficial uses of the Fisher/Carpenter basin in order to meet State Water Quality Standards for temperature, fecal coliform bacteria, and dissolved oxygen as part of the total maximum daily load.  A slate of community supported restoration and/or enhancement projects will be developed which, when implemented, will improve water quality, provide more consistent stream flows, restore some historic hydrologic function and support fish and wildlife habitat.

# 2	Watershed Delineation

## 2.1	Boundaries

The characterization project area, Fisher/Carpenter Creek Watershed, is a 16,320-acre (25.5 square miles) watershed that drains into the south fork of the Skagit River on the southwestern edge of Skagit County, Washington (Figure 2.1).  The Fisher/Carpenter Creek Watershed extends 8.1 miles in a north to south orientation, is 3.7 miles wide, and is bounded by the 10-foot Hill Ditch levee on the west side, the City of Mount Vernon and Little Mountain to the north, Big Lake to the east, and the Pilchuck Creek Watershed to the south.  The majority of the watershed (14,325 acres or 87 percent) is located in Skagit County.  The remaining 1,955 acres or 13 percent is located in Snohomish County.  The Fisher/Carpenter Creek Watershed was defined by standard watershed delineation techniques using topography and field investigations to identify areas that affect flow direction.

## 2.2	Topography

The topography of the Fisher/Carpenter Creek Watershed ranges from mean sea level (MSL) to approximately 1,700’ above MSL and has primarily three distinguishing topographic features:  the alluvial flats of the Skagit River Delta, a long north-south trending ridge that peaks at 1,727-foot high Devils Mountain, and associated rolling uplands.  Several creeks drain the watershed, including English, Carpenter, Stackpole, Lake Ten, Sandy, Johnson, and Bulson (collectively known as the “Carpenter Creek” system), and Starbird, Fisher and Little Fisher Creeks (collectively known as the “Fisher Creek” system) (Figure 2.2).

Water from the Carpenter Creek system flows into Hill Ditch, where it combines with flows from the Fisher Creek system to form Fisher Slough.  Fisher Slough drains to the south fork of the Skagit River through a large tidegate located about a mile south of the town of Conway, Washington.

Figure 2.1 State Map With FCC Location

Figure 2.2 Watershed Boundary, Roads, and Streams

# 3	Land Use

## 3.1	Relevant Historical Land Use

Native American habitation in the Skagit Delta area is documented as far back as 5,000 years ago (Weisberg and Riedel, 1991).    European settlers arrived in the late 1800s and built levees using horses, wagons and ship scraps in order to create productive farmland.  According to local pioneer Harry Johnson, by 1909, the first diking and drainage district was formed.

Collins and Sheikh, 2003, mapped the pre-settlement vegetation of the Skagit Delta from historic records.  In the historic maps, the flats area of the watershed was primarily wetlands, channels, ponds, and forested floodplain [(Collins and Sheikh)].  In the New Map of the Puget Sound Country Fifth Revised Edition, 1903, obtained from the Skagit Historical Museum much of the farmland that is to the west of the Fisher Carpenter Creek Watershed was once a wetland.  This map also denotes the area as very good hayland.  A 1911 topographic map of the Fisher/Carpenter Creek Watershed shows the Carpenter Creek system exiting through the town of Fir now referred to as Conway.    A dominant feature on early maps of the watershed is the English Lumber Company Rail Road.  The English Lumber Company was a large employer of loggers at the turn of the twentieth century and, according to Harry Johnson, the English Logging Company had ten different logging camps running full steam in and around the Cederdale area until they ran out of logs and moved on.

## 3.2	Existing Land Use/Zoning

Ninety-one percent of the land use in the Fisher/Carpenter Creek Watershed is categorized as Rural, Forest, and Agriculture.  The Mount Vernon Urban Growth Area and the City of Mount Vernon make up the other 8% with less than 1% lakes and ponds.

Table 3.2   Zoning designations, acreages and percentage of land use in Fisher/Carpenter Creek Watershed (2007).

| FCC Skagit County Land use | Area (Acres) | *Percent of Watershed |
| --- | --- | --- |
| Rural Reserve (RRv) | 5348 | 38% |
| Industrial Forest (IF-NRL) | 3344 | 24% |
| Secondary Forest (SF-NRL) | 2822 | 20% |
| City (CTY) | 731 | 5% |
| Rural Intermediate (RI) | 548 | 4% |
| Rural Resource (RRc-NRL) | 488 | 3% |
| Urban Growth Area (UGA) | 338 | 2% |
| Agriculture (Ag-NRL) | 241 | 2% |
| Rural Business (RB) | 8 | <1% |
| Water | 88 | <1% |
| Total | 13956 | 100% |

*Percent rounded to the nearest whole number

Rural Reserve

The majority of the land (thirty eight percent) in the Fisher/Carpenter Creek Watershed is zoned Rural Reserve.  According to Skagit County, the purpose of the Rural Reserve is to allow low-density development and preserve the open space of areas that are transitioning between resource lands and non-resource lands.

Industrial Forest

Industrial Forest is the second largest zoning area making up 24% of the Fisher/Carpenter Creek Watershed in Skagit County.  According to Skagit County, the purpose of the Industrial Forests Natural Resource Lands District is to ensure that forest lands of long-term commercial significance are conserved and managed to provide sustainable forest yields, job stability, ecological values and the continuation of a viable commercial forest industry in Skagit County.  Conservation of forest resources must be assured through measures designed to prevent incompatible development on or adjacent to resource lands.  Forest activities shall not constitute a nuisance if conducted in accordance with the State Forest Practice Rules and Regulations.

Secondary Forest

Secondary Forests comprise the third largest zoning area in the Fisher/Carpenter Creek Watershed in the Skagit Valley.  The purpose of the Secondary Forest – Natural Resource Lands (SF-NRL) District is to provide a transitional area between the Industrial Forest - Natural Resource Lands zone and Rural zoned lands designated primarily for residential use and other non-forestry uses.  The SF- NRL zone also provides a zoning district where smaller scale timber and other resource management activities can occur while providing protection from encroachment of residential activity that may encumber standard forest practices.

Rural Intermediate

The purpose of the Rural Intermediate district is to provide and protect land for residential living in a rural atmosphere, taking priority over resource land uses.

Rural Resource

The Rural Resource designation makes up 3% of the land use within the Fisher/Carpenter watershed.  The purpose of the Rural Resource district is to recognize and encourage the conservation of lands with long-term commercial agriculture or forestry significance.  These lands provide support for the industrial natural resource land base and are managed on a smaller scale than the industrial resource lands due to poorer soils and smaller parcel size.

UGA

Approximately 2% of the watershed is zoned UGA or Urban Growth Area.  The purpose of this zone is to permit development in unincorporated Mount Vernon including issuing development permits and subdivision of property under the requirements of the Growth Management Act.

Agriculture

Two percent of the land use in this watershed is zoned Agriculture.  This area is mainly flat land with highly productive soil.  The purpose of this designation is to provide for continuing farming activities and operations and to conserve the agricultural land, which is considered the essence of the County’s character.

Rural Business

The Rural Business zone makes up less than 1% of this watershed.  The purpose of this district is to provide expansion and use opportunities for existing isolated nonresidential uses that provide jobs opportunities for rural residents.

There are only two commercial and industrial areas in the watershed.  Meridian Aggregate leases a portion of a large quarry on land owned by the City of Mount Vernon at the east end of Hickox Road.  Wilder Construction Company owns a gravel quarry on State Route 534, about five miles east of Conway.

Over seventy-five percent of the land in Fisher/Carpenter Creek Watershed located in Snohomish County is zoned Rural Five.  This designates the area to be subdivided into a minimum of five acres.

Figure 3.2 Zoning in the Fisher/Carpenter Creek Watershed

3.3 	Sewer and Water Utilities

There is currently no sanitary sewer service in the Fisher/Carpenter Creek Watershed. There were about 777 septic sites mapped within the Fisher/Carpenter Creek Watershed in 1999.  According to Skagit County GIS data, installation of septic sites has increased over the years with development.

Figure 3.3 Septic Absorption Fields in the Fisher/Carpenter Creek Watershed

# 4	Soils

## 4.1	Soils Description

The USDA Soil Survey of Skagit County identifies 40 soil types (Figure 4.1) in the Fisher/Carpenter Creek Watershed (Soil Conservation Service, 1989).  These can be grouped into seven general categories:  Barneston/Dystric Xerorthents, Tokul/Dystic Xerochrepts, Vanzandt, Chuckanut/Cathcart, Coveland, Jug, and Kindy. The majority of the soils in the Fisher/Carpenter Creek Watershed are formed on glacially modified hills.  The soils are moderately well drained.  They formed in volcanic ash and loess underlain by glacial till.  The surface is covered with a mat of needles, leaves, and twigs.  The surface layer and subsoil are gravelly loam about 34 inches thick.  The substratum is gravelly sandy loam about 5 inches thick over silica-cemented glacial till.  Depth to silica-cemented glacial till ranges from 20 to 40 inches.   Figure 4.1 shows the locations of the various soil types.  Table 4.1 lists relevant physical characteristics of each.

Figure 4.1 Soils of the Fisher/Carpenter Creek Watershed

Table 4.1 Characteristics of Fisher/Carpenter Creek soil types.

| Soil # | Soil Name | Slope | Hydrologic Group | Drainage/Septic Tank Absorption Fields | Depth (in.) | USDA Topsoil Texture |
| --- | --- | --- | --- | --- | --- | --- |
| 4 | Tokul-Skipopa-Dystric | 0-90% | B | Severe: slope | 0-3” | Gravelly silt loam |
|  | Xerochrepts |  |  |  | 3-24” | Very gravelly loam, very gravelly |
|  |  |  |  |  |  | sandy loam, gravelly silt loam |
| 5 | Barneston gravelly | 0-65% | B | Severe: poor filter | 0-5” | Gravelly loam |
|  | loam |  |  |  |  |  |
| 6 | Barneston gravelly sandy loam | 8-30% | B | Severe: poor filter, slope | 0-5” | Very gravelly sandy loam |
| 7 | Bow-Coveland | 30-65% | B | Severe: poor filter, slope | 0-5” | Very gravelly sandy loam |
| 10 | Bellingham Silt loam | 0-3% | D | Severe: wetness, percs slowly | 0-9" | Silt loam |
| 11 | Bellingham mucky silt | 0-2% | D | Severe: ponding, percs slowly | 0-9” | Mucky silt loam |
| 16 | Bow gravelly loam | 0-3% | D | Severe: wetness, percs slowly | 0-7" | Gravelly loam |
| 17 | Bow gravelly loam | 3-8% | D | Severe: wetness, percs slowly | 0-7" | Gravelly loam |
| 22 | Cathcart | 8-15% | B | Moderate: percs slowly, slope | 0-10” | Loam |
| 23 | Cathcart loam | 15-30% | B | Severe: slope | 0-10” | Loam |
| 24 | Cathcart loam | 30-65% | B | Severe: slope | 0-7” | Loam |
| 27 | Chuckanut gravelly | 8-30% | B | Severe: slope | 0-9” | Gravelly loam |
|  | loam |  |  |  |  |  |
| 28 | Chuckanut gravelly | 30-65% | B | Severe: slope | 0-9” | Gravelly loam |
|  | loam |  |  |  |  |  |
| 34 | Cokedale silt loam | 0-3% | D | Severe: flooding, wetness, | 0-27” | Silt loam |
|  |  |  |  | poor filter |  |  |
| 39 | Crinker-Rock outcrop | 3-30% | C | Severe: depth to rock, slope | 0-20” | Very channery silt loam |
|  | complex |  |  |  |  |  |
| 48 | Dystric Xerochrepts- | 65-90% | C | Severe: depth to rock, slope | 0-39” | Very gravelly loam |
|  | Rock outcrop complex |  |  | large stones |  |  |
| 67 | Hoogdal silt loam | 8-15% | C | Severe: wetness, percs slowly | 0-6" | Silt loam |
| 69 | Hoogdal silt loam | 30-60% | C | Severe: wetness, percs slowly | 0-6” | Silt loam |
| 72 | Hydraquents tidal | 0-1% | D | Severe: flooding, ponding | 0-6” | Fine sandy loam |
| 74 | Illabot very gravelly |  | C | Severe: cemented pan, | 0-9” | Very gravelly loam |
|  | loam |  |  | wetness, slope |  |  |
| 77 | Jug very gravelly loam | 0-3% | A | Severe: poor filter, slope | 0-7 | Very gravelly loam |
| 80 | Kindy gravelly silt loam | 3-30% | C | Severe: cemented pan, | 0-4” | Gravelly silt loam |
|  |  |  |  | wetness, slope. | 4-19” | Very gravelly loam, very gravelly |
|  |  |  |  |  |  | silt loam |
| 81 | Kindy gravelly silt loam | 30-65% | C | Severe: cemented pan, | 0-4” | Gravelly silt loam |
|  |  |  |  | wetness, slope. | 4-10” | Gravelly loam, gravelly silt loam, |
|  |  |  |  |  |  | Very gravelly silt loam |
| 97 | Mukilteo muck | 0-1% | C | Severe: ponding | 0-5” | Muck |
|  |  |  |  |  | 5-48” | Hemic material |

| Soil # | Soil name | Slope | Hydrologic Group | Drainage/Septic Tank Absorption Fields | Depth (in.) | USDA Topsoil Texture |
| --- | --- | --- | --- | --- | --- | --- |
| 102 | Norma silt loam | 0-3% | D | Severe: ponding | 0-11” | Silt loam |
| 106 | Pits | n/a | C | n/a | n/a |  |
| 123 | Skagit silt loam | 0-1% | D | Severe: depth to rock, slope | 0-12 | Silt loam |
| 124 | Skipopa silt loam | 0-3% | D | Severe: wetness, percs slowly | 0-8" | Silt loam |
| 125 | Skipopa silt loam | 3-8% | D | Severe: wetness, percs slowly | 0-8" | Silt loam |
| 136 | Sumas silt loam | 0-2% | D | Severe: wetness, poor filter | 0-6” | Silt loam |
| 143 | Terric Medisaprists | 0-2% | D | Severe: ponding, percs slowly | 0-17" | Muck |
| 146 | Tokul gravelly | 0-8% | C | Severe: cemented pan, | 0-2” | Gravelly loam |
|  | loam |  |  | wetness | 2-34” | Gravelly loam, gravelly silt loam |
| 147 | Tokul gravelly | 8-15% | C | Severe: cemented pan, | 0-4” | Gravelly loam |
|  | loam |  |  | wetness | 4-28 | Gravelly loam, gravelly silt loam |
| 148 | Tokul gravelly | 15-30% | C | Severe: cemented pan, | 0-2” | Gravelly loam |
|  | loam |  |  | wetness, slope | 2-26” | Gravelly loam, gravelly silt loam |
| 149 | Tokul gravelly | 30-65% | C | Severe: cemented pan, | 0-2” | Gravelly loam |
|  | loam |  |  | Wetness, slope | 2-25” | Gravelly loam, gravelly silt loam |
| 153 | Vanzandt very | 0-15% | C | Severe: wetness | 0-6” | Very gravelly loam |
|  | gravelly loam |  |  |  |  |  |
| 154 | Vanzandt very | 15-30% | C | Severe: cemented pan, | 0-6” | Very gravelly loam |
|  | gravelly loam |  |  | wetness, slope |  |  |
| 155 | Vanzandt very | 30-65% | C | Severe: cemented pan, | 0-6” | Very gravelly loam |
|  | gravelly loam |  |  | wetness, slope |  |  |
| 158 | Winston gravelly | 0-8% | B | Severe: poor filter | 0-6” | Gravelly silt loam |
|  | silt loam |  |  |  |  |  |
| 165 | Xerorthents | 0-5% | C | Severe: wetness | 0-60” | Variable |

Due to the cemented pan on many of the Fisher/Carpenter Creek soils, winter rains tend to run off quickly after the surface layer is saturated.  Consequently, the creeks and tributaries of the Fisher/Carpenter Watershed typically have “flashy” hydrology patterns.

# 5	Geohydrology

The groundwater system that occurs within the Fisher/Carpenter Creek Watershed is quite variable in its water supply yield and geographic distribution.  This chapter reviews data from selected water supply well drilling logs to illustrate the range of geohydrology conditions in the Watershed.

## 5.1	Aquifer

A random review of well drilling logs within each section of the Fisher/Carpenter Creek Watershed, on record with the Department of Ecology (Figure 5.1), indicates that water supply wells in the watershed typically tap a production aquifer.  The aquifer is located in sand, gravel, clay strata or boulders, which is confined from above by a clay stratum.  Depending on the ground surface elevation of the well, the wells tap the static water level at depths ranging from 7 feet to 375 feet below the surface.  Table 5.1 shows locations of selected water supply wells from Department of Ecology’s well log database.  One well log site was selected per section of land to document soils location of the aquifer.  Appendix 3 shows driller well logs of these wells located within the Watershed.

Figure 5.1 Well Log Locations (courtesy of Washington State Department        of Ecology)

Aquifer yield varies widely within the relatively small geographic areas.  At one residential building site on Bulson Road, the depth of the well was dug to a level of 300+ feet before water was found.  The 300-foot source was not consistent; therefore the well driller was forced to drill to a depth of 500 feet, while a nearby neighbor has a very productive well at 140 feet. (Jantz, personal interview)  The available well logs reflect this variability in aquifer yield, as many well logs were reported to find no water.

# 6     Surface Water Hydrology

## 6.1	Description of Sub-basins

The Fisher/Carpenter Creek Watershed drains an area of about 25.5 square miles (16,320 acres) Figure 6.1.  Ten separate sub-basins were identified within the watershed.  The sub-basins were delineated based on the local topography and conveyance routes (such as ditches and creeks) within the existing drainage system.  Skagit Conservation District field-checked the majority of the sub-basin and adjusted the boundaries slightly to better represent the actual drainage conditions within the watershed.  The sub-basins are listed in Table 6.1. Figure 6.1 shows the locations of the sub-basins.    Wetland features are discussed in Section 6.4

Table 6.1 Summary of Drainage Sub-basins Within the Fisher/Carpenter Creek Watershed

| Sub-basin | ID No. | Approx. Area (Acres) | *Percent of Total Area |
| --- | --- | --- | --- |
| Stackpole | 1 | 873 | 5% |
| English | 2 | 843 | 5% |
| Carpenter | 3 | 1770 | 11% |
| Lake Ten | 4 | 611 | 4% |
| Sandy | 5 | 1031 | 6% |
| Johnson | 6 | 1068 | 7% |
| Bulson | 7 | 4480 | 27% |
| Starbird | 8 | 1957 | 12% |
| Big Fisher | 9 | 2335 | 14% |
| Little Fisher | 10 | 1800 | 11% |

* Percent rounded to the nearest whole number

Figure 6.1 Sub-basin Boundaries in the Fisher/Carpenter Creek Watershed

Northern Drainage

Stackpole Creek Sub-basin (No. 1)

The Stackpole Sub-basin consists of the lower southern slopes of Little Mountain, an area accessed by the eastern portion of East Hickox Road, the southern end of Blodgett Road, Arbor Lane, Shale Drive, Valley Ridge Lane, Mountain Ridge Drive, and Pamela Street.  This area is primarily residential on half-acre up to 5-acre lots and is zoned to be a higher-density Urban Growth area for the City of Mount Vernon.  Wetland conditions exist in some of the areas that remain forested between Valley Ridge Lane and Pamela Street down to the northern portion of East Stackpole Lane. The headwaters of Stackpole Creek begin in a semi-forested area.  Runoff travels through residential areas through roadside ditches before concentrating at two culverts under East Hickox Road.  South of East Hickox Road, runoff is channelized in two ditches through farm fields and poplar plantations before crossing East Stackpole Road and flowing into Carpenter Creek at Cascade Ridge Drive.

Carpenter Creek Sub-basin (No. 2)

The Carpenter Creek Sub-basin is the most northern sub-basin in the Fisher/Carpenter Creek Watershed.  It contains all the land between the eastern slopes of Little Mountain Park in Mount Vernon in the west and the Nookachamps/Big Lake Watershed divide in the east.  The headwaters of Carpenter Creek include part of Mount Vernon’s Eaglemont Golf Course, as well as wetland areas along Little Mountain Road.  Runoff originating near Eaglemont Golf Course drains through a series of beaver ponds and man-made ponds before flowing under Little Mountain Road.  South of Little Mountain Road, Carpenter Creek joins English Creek and flows through pastures and beaver swamps before entering a relatively pristine forest area east of Little Mountain.

English Creek Sub-basin (No. 3)

The English Creek sub-basin drains the area between the north slope of Devils Mountain and Little Mountain Road.  Virtually all of the land in this sub-basin is used for industrial forestry, with a few scattered residences along Ervine Road, the sub-basin’s only major road.  This sub-basin is largely a forested area and believed to be in a semi-natural state.

Lake Ten Creek Sub-basin (No. 4)

The Lake Ten Creek sub-basin originates at Lake Ten, a small natural lake located high on the north slope of Scott Mountain.  Lake Ten Creek flows steeply down through industrial forestland and then through the Cascade Ridge subdivision.  After crossing through culverts on Cascade Ridge Road and Grouse Drive, the creek flows into Carpenter Creek just upstream of the intersection of Cascade Ridge Road and Stackpole Road.  While available maps indicate that the confluence is located downstream of the road junction, SCD field observations indicate that the creek was re-routed to its current upstream confluence relatively recently.

Sandy Creek Sub-basins (No. 5)

The Sandy Creek sub-basin collects runoff from several small tributaries and beaver ponds that drain the south slopes of Scott Mountain (Figure 4.1).  At the mouth of its steep ravine, Sandy Creek crosses Kanako Lane.  While originally the creek flowed directly west from the ravine across an alluvial fan to Carpenter Creek, many years ago it was diverted into a ditch running alongside Kanako Lane.   The ditch runs north for several hundred feet to its confluence with Hill Ditch at the Kanako Lane Bridge.  The Skagit County Department of Public Works dredges the confluence at regular intervals, attesting to the frequent high sediment bed load carried by Sandy Creek.

Johnson Creek Sub-basin (No. 6)

The headwaters of Johnson Creek begin at a beaver pond on the east side of Scott Mountain then flow west.  There are very few tributaries to Johnson Creek and its flows are very irregular.  From the beaver ponds, Johnson Creek flows west where it encounters large boulders and many trees that have fallen into the creek, due to the steep banks and logging that had taken place on Johnson Creek over 20 years ago.  Further downstream, Johnson Creek encounters a system of waterfalls over 100 feet in height that make salmon inaccessible to the upper reaches.  At the mouth of Johnson Creek, the creek bed has been routed along the base of the hill, and because of the irregular stream flows and sediment runoff, the streambed has been filling up with gravel deposited by the creek.  Fifteen years ago, the creek was dredged and kept at an average of 5 feet below the level of East Johnson Road.  Its sediment bed load has raised the level of the creek bed above the level of the road and threatens to wash out the road with each high water.  Johnson Creek crosses East Johnson Road and enters the Hill Ditch system on the north side of East Johnson Road.

Southern Drainage

Bulson Creek Sub-Basin (No. 7)

The Bulson Creek Sub-basin, which is the largest sub-basin of the Fisher/Carpenter Creek Watershed, is drained by three distinct forks of Bulson Creek.  The northern fork of Bulson Creek begins east of Lake Sixteen and travels west past Lake Sixteen where it travels under Lake Sixteen Road and continues west through low density housing on its west bank.  The northern fork of Bulson Creek then passes through a forest and enters the higher density development of Hermway Heights where it spills over a 100-foot waterfall, winds around another forested area, and enters into the southern fork of Bulson Creek.

The center fork of Bulson Creek begins south of Highway 534 at the topographic divide approximately one mile west of Lake McMurray and flows west along Highway 534.  The creek winds through extensive scrub-shrub and forested wetlands along the south side of the highway before meeting up with the southern fork of Bulson Creek north of English Road.

The headwaters of the southern fork of Bulson Creek are near Starbird Road in south Skagit County.  The south fork works its way north through an area of small “hobby” livestock farms and emergent and forested wetlands, where it passes under English Road and is joined by the middle fork of Bulson Creek. After joining with the middle fork of Bulson Creek the stream crosses State Route 534 in a large fishway project created by the Washington State Department of Fish and Wildlife. The stream continues north, with good overall riparian habitat, where it is joined by the northern section of Bulson Creek and enters Hill Ditch.

Starbird Creek Sub-Basin (No. 8)

The headwaters of Starbird Creek begin on the ridge approximately one mile west of Lake McMurray and travel west through forestland before crossing Starbird Road.  The creek then passes through the Fremali residential subdivision and crosses Fremali Lane with a narrow buffer of alder and spirea.  Horses and sheep are pastured to the south of this crossing in an area with little or no riparian vegetation.  Downstream of Fremali Lane, the stream passes on the east side of Starbird Creek Lane. At this point the channel’s forested riparian habitat provides ample shade to the stream with large cedar trees.  Further downstream, the creek passes under Bulson Road and goes through a palustrine forested seasonal wetland and enters the main stem of Big Fisher Creek.

Big Fisher Creek Sub-basin (No. 9)

The headwaters of the Big Fisher Sub-basin begin in Snohomish County on the forested ridge approximately one mile south west of Lake McMurray.  The northern fork of Big Fisher begins in forested lands and then enters a small beef farming operation before crossing English Grade Road under a high wooden trestle bridge.  The creek then loops south across 324th Street NW, and joins the southern fork of Big Fisher Creek.

The southern fork of Big Fisher Creek begins as a wetland in northern Snohomish County and travels west through forestland where it crosses 24th Avenue NW.  The southern fork of Big Fisher Creek then passes across English Grade Road through pastureland, meeting up with the north fork of Big Fisher before crossing Brandstrom Road.  From Brandstrom Road, Big Fisher Creek passes through open pastureland where it crosses 324th Street NW, heading northwest just to the west of a natural gas pipeline through more open cattle pasture, crossing 44th Avenue NW and entering Skagit County north of West Bulson Road.   Big Fisher Creek continues to flow northwest through more pasture areas for approximately one half mile north of West Bulson Road where it enters into a wooded area crossing Starbird Road.  In the late 1990s, Skagit County constructed a log weir fishway to provide fish access upstream of the Starbird Road culvert.

From the fishway, Big Fisher Creek continues northwest through a partially forested riparian area along a cleared natural gas pipeline right-of-way.  Downstream, it passes over the natural gas pipeline.  From this point on, Big Fisher Creek enters a heavily forested gorge and runs about one mile before re-emerging under Cedardale Road in a large fishway and flows under I-5.  It then flattens out for its final reach, under Franklin Road, and through forested bottomlands to its confluence with Hill Ditch at Fisher Slough Bridge.

Little Fisher Creek Sub-basin (No. 10)

The headwaters of Little Fisher Creek begin south of 324th Street NW in a wetland area.  The east fork flows northwest under 324th Street where it travels through a forested area for approximately one mile to the County Line Road/332 Street NW.  From the County Line Road, the stream crosses Brunn Road where it passes along a low-density housing area. The east fork of Little Fisher Creek then crosses Pacific Highway where it is joined by a tributary that drains fields east of I-5.  After joining with the tributary, the east fork of Little Fisher Creek passes under Milltown Road along the north side and then travels under Bonnie View Road.  From Bonnie View Road, the east fork of Little Fisher continues northwest through a Rural Reserve zoned area with ample riparian forest habitat and crosses Clarence Lane.  From Clarence Lane, the east fork of Little Fisher Creek crosses Franklin Road.  Heading downstream, the east fork of Little Fisher Creek passes through a pasture, where it is joined by the west fork of Little Fisher Creek and flows into the Hill Ditch system and Fisher Slough.

The west fork of Little Fisher Creek begins in a seasonal wetland just east of 68th Avenue NW, and travels northwest where it crosses 324th Street NW.  From 68th Avenue NW, the stream continues through a forested area to a pond impounded by a small concrete dam just upstream of 332nd St NW.  Below the dam, the creek flows under the County Line Road/332nd Street NW then flows north to Milltown Road.  From Milltown Road, the creek flows through a small wood weir fishway and winds into a small-forested valley where it is joined by the east fork of Little Fisher Creek.  It then flows northwest through a pasture where it runs along a dike out to the Hill Ditch system/Fisher Slough.

## 6.2	Impervious Surfaces

Impervious surfaces are compressed soils or sealed surfaces such as rooftops, sidewalks, roads, and parking lots that prevent infiltration of precipitation into the soils.  The relative proportion of impervious surface in a watershed affects the quantity and timing of surface runoff, aquifer recharge, and quality of receiving water.  Detrimental effects such as stream enlargement and widening, erosion, down cutting, decreased channel stability, and embeddedness begins to occur in watersheds with 10% or greater impervious cover (Schuler, 1994).  Impervious surface areas in the Fisher/Carpenter Creek Watershed were delineated in a Geographic Information System (GIS) map from 2002 aerial photography (Figure 3.3).  Areas included as impervious were roads (not including gravel areas), rooftops, and driveways.  The impervious surfaces were calculated for each of the 10 sub-basins in the watershed (Table 6.2).  437 acres of the watershed, or roughly 3% overall is made up of impervious surface.

| Sub-basin | Sub-basin number | Sub-basin size | Sub-basin Impervious Surface acres | *Percent Impervious Surface per sub-basin |
| --- | --- | --- | --- | --- |
| Stackpole | 1 | 873 | 35.2 | 4% |
| English | 2 | 843 | 2.1 | 0% |
| Carpenter | 3 | 1770 | 33 | 2% |
| Lake Ten | 4 | 611 | 30 | 5% |
| Sandy | 5 | 1031 | .5 | 0% |
| Johnson | 6 | 1068 | 3.2 | 0% |
| Bulson | 7 | 4480 | 133 | 3% |
| Starbird | 8 | 1957 | 24.5 | 1% |
| Big Fisher | 9 | 2335 | 60.5 | 3% |
| Little Fisher | 10 | 1800 | 115 | 6% |

Table 6.2 Impervious surface area is shown for each sub-basin.

Figure 6.2 Impervious Surfaces in the Fisher/Carpenter Creek Watershed

## 6.3	Flow

Local hydrologic conditions are a function of the quantity, intensity, and timing of runoff from each of the sub-basins within the Fisher/Carpenter Creek Watershed.

In 2000 the Department of Ecology (Pitz and Garrigues) performed a study to develop a map that summarized streamflow in the basin during late summer, low-flow conditions. Depending on the estimated accuracy of the flow measurements, a second objective of the study was to develop a preliminary understanding of the streamflow gains and losses along the main stem of Carpenter Creek (also known as Hill Ditch).  In this study, 11 monitoring stations were placed on Hill Ditch and many of the Hill Ditch tributaries such as Stackpole, Carpenter, Sandy, Johnson, Bulson, and Big Fisher Creeks as shown in Table 6.3a.  The study shows that the low flow rates are consistent with the large drainage area that is located over a low permeability geologic setting.  This suggests that dry-season groundwater baseflow contributions to streams will be limited in scale.  Tributary contributions to the Carpenter Creek/Hill Ditch main stem are likely controlled in large part by groundwater fracture flow within the upland bedrock. (Washington Department Of Ecology)

Table 6.3a Washington State Department of Ecology snapshot of stream flows on September 21, 2000 from 7:45 a.m. to 5:00 p.m.

| Station # | Station Name | Measurement Time | Estimated Stream Flow (cfs) |
| --- | --- | --- | --- |
| FC-1 | Hill Ditch under northbound 1-5 bridge | 7:45 | 2.22 |
| FC-2 | Hill Ditch under Conway Hill Road bridge | 8:45 | 0.85 |
| FC-3 | Hill Ditch below Bulson Creek | 9:50 | 1.03 |
| FC-4 | Bulson Creek below Bulson Road | 10:45 | 0.84 |
| FC-4 | Bulson Creek below Bulson Road | 10:55 | 0.86 |
| FC-5 | Hill Ditch below Johnson Creek | 11:45 | 0.28 |
| FC-6 | Johnson Creek | 12:15 | 0.06 |
| FC-7 | Sandy Creek | 1:35 | 0.15 |
| FC-8 | Carpenter Creek below Sandy Creek | 2:00 | ~0.7 |
| FC-9 | Carpenter Creek below Lake Ten Creek | 3:25 | 0.51 |
| FC-10 | Stackpole Creek | 3:45 | 0.07 |
| FC-11 | Fisher Creek at fish ladder | 5:00 | 0.5 |
|  | Ten Lake Creek |  | 0.5 |
|  | Carpenter Creek above Stackpole Creek |  | ~0.05 |
|  | Fisher/Carpenter Creek below confluence |  | ~0.3 |

To elaborate on the Department of Ecology’s streamflow conditions, standard USGS regression equations were used to model typical apportionments of runoff flows from each sub-basin during various rainfall conditions.  The estimates are shown in Table 6.3. (WSDOT, 1997)

In all three of the regression equations Sub-basin No. 7 (Bulson Creek) is the largest contributor to the Hill Ditch system with more than 28% of the flow contributing to the Fisher/Carpenter Creek Watershed during the 2, 25 and 100 year flows.

Table 6.3b Two year, twenty-five year, and one hundred year flow estimates by USGS regression equations.

| Sub-basin Name | Sub-basin Area (mi2) | 2 Year | 25 year | 100 year |
| --- | --- | --- | --- | --- |
|  |  | Q (cfs) | % Flow Total Watershed | Q (cfs) | % Flow Total Watershed | Q (cfs) | % Flow Total Watershed |
| Stackpole Creek | 1.36 | 25 | 6.9% | 55.0 | 7.0% | 71.9 | 7.1% |
| English Creek | 1.61 | 29 | 8.0% | 63.7 | 8.1% | 83.2 | 8.3% |
| Carpenter Creek | 2.77 | 47 | 12.8% | 101.8 | 13.0% | 132.7 | 13.2% |
| Lake Ten Creek | 0.95 | 19 | 5.0% | 40.4 | 5.1% | 52.8 | 5.2% |
| Sandy Creek | 1.36 | 25 | 6.9% | 55.0 | 7.0% | 71.9 | 7.1% |
| Johnson Creek | 1.67 | 30 | 8.2% | 65.7 | 8.4% | 85.8 | 8.5% |
| Bulson Creek | 7.00 | 106 | 28.9% | 226.7 | 29.1% | 294.8 | 29.2% |
| Hill Ditch Total | 16.72 | 228 | 62.1% | 481.1 | 62.0% | 623.9 | 61.9% |
| Starbird Creek | 3.06 | 52 | 14.0% | 110.9 | 14.2% | 144.6 | 14.3% |
| Fisher Creek | 3.65 | 60 | 16.3% | 129.2 | 16.5% | 168.3 | 16.7% |
| Little Fisher Creek | 2.81 | 48 | 13.0% | 103.0 | 13.2% | 134.4 | 13.3% |
| Fisher Creek Total | 9.52 | 139 | 37.9% | 295.7 | 38.0% | 384.2 | 38.1% |

Notes:  A standard Mean Annual Precipitation of 35 inches was used.  Road diverts some flow on Lake Ten Creek.

Standard error for equations are 2 yr. return period=56% / 25 yr. Return period=53% / 100 yr. Return period=54%

## 6.4	Channel Morphology

There are four principle types of channel morphology in the Fisher/Carpenter Creek Watershed:  drainage ditches in upland areas, natural creek channels, manmade creek channels, and sloughs.

Drainage Ditches

Maintained drainage ditches run along one or both sides of most of the roads within the watershed.  Ditches in which water velocities are high enough to erode the banks are armored with rock.  For example, Cascade Ridge, which is steep and conveys a large quantity of runoff, is the most heavily armored in the watershed.  Lower gradient ditches are typically unlined.  The Skagit County Public Works Department dredges sediment and vegetation from the unlined ditches along the arterial roads in the Watershed about once a year, typically in the spring.  There are also several unlined ditches through pasture and forest areas that connect to either roadside ditches or directly to a waterway; this is especially true in the Fisher Creek Sub-basin.

Natural Creek Channels

Carpenter, English, Lake Ten, Sandy, Johnson, Bulson, Fisher, and Starbird Creeks contain varying degrees of natural channel morphology.  These tributaries will be discussed in the following sections.

Carpenter Creek (Basin No. 2), the section of creek from south of Little Mountain Road to Cascade Ridge Road is in a natural state with very few crossings and an average bank full width of six feet and an average bank full depth of 4-12 inches. The area of stream south east of Little Mountain contains large woody debris, gravel bars, riffles, pools, and generally good connection with the flood plain upstream of E. Hickox Road.  Downstream of E. Hickox Road, the stream channel begins to become slightly more eroded and at one location has its banks armored with concrete columns and rebar.  There are also tires and other debris downstream of East Hickox Road.  Downstream of the Cascade Ridge Road culvert, the stream passes into the man-made Hill Ditch system.

English Creek (Basin No. 3), the section of creek above Ervine Road is in a natural state having very few crossings before the creek crosses Ervine Road and into the designated Rural Reserve zoning area.  The streambed is primarily medium gravel with an average bank full width of ten feet and an average bank full depth of one foot.

Lake Ten Creek (Basin No. 4)  begins at  Lake Ten and flows down through a recently logged forest area with a functioning riparian area to Cascade Ridge Road. Downstream of Cascade Ridge Road, Lake Ten Creek crosses Grouse Drive and proceeds west through a forested area that is currently being logged.   It is then joined by Carpenter Creek.  The mouth of Lake Ten Creek is about 150 feet upstream of Cascade Ridge Drive.  It contains a bank full width of 3 feet, a bank full depth of 18 inches and has a forest cover and very little erosion.

Sandy Creek (Basin No. 5) an undisturbed section of stream from the headwaters down to Kanako Lane.  The streambed is primarily gravel where it crosses Kanako Lane in a 4-foot corrugated metal pipe culvert.  The bank full width at this culvert is 6 feet with a bank full depth of 18 inches.  The creek then enters a roadside ditch where there is little to no riparian habitat before entering the Hill Ditch system.

Bulson Creek (Basin No. 7) has varying degrees of undisturbed channels at the headwaters of the north, middle and south fork.  Above Lake Sixteen, the north tributary of Bulson Creek channel contains high amounts of gravel substrate as it meanders through a valley of mature fir and cedar trees.  As the stream crosses Lake Sixteen Road, it travels behind a group of summer cabins on its right bank that has been converted into year around residences.  The stream at this point has a floodplain width of 25 feet, a bank full width of 20 feet and a bank full depth of one foot.  The north fork of Bulson Creek then re-enters a forest where it passes over a 100 foot waterfall, joining with the south fork of Bulson Creek where the bank full width is 10 feet, the bank full depth is 18 inches and the floodplain width is 50 feet, making it’s way down to Bulson Road.  After Bulson Road, Bulson Creek passes by a dairy farm before joining with Hill Ditch.

The middle tributary passes next to State Route 534 where it enters the south fork of Bulson Creek.  Because the floodplain is constricted by the highway fill prism, this is the most modified of the three tributaries of Bulson Creek.  There are four smaller tributaries that flow into the middle fork of Bulson Creek that appear to be unmodified. The middle fork of Bulson Creek is joined by the south fork of Bulson Creek downstream of English Road.

The south fork of Bulson Creek begins south of Bulson Road and travels north through various wooded wetlands and pasturelands before crossing Bulson Road and entering a densely forested area.  The creek then passes under English Road with a bank full width of seven feet, a bank full depth of eight feet and a floodplain width of 20 feet.  The creek is contained by a deep ravine (approximately 75 feet deep) at this point with a heavily forested riparian area on both sides.  Downstream of English Road the south fork is joined by the middle tributary of Bulson Creek and crosses Highway 534.  The stream has a 14-foot bank full width, a 12-inch bank full depth, and floodplain of 100 feet with acedar and salmonberry growing in the riparian area.  Downstream of Highway 534, the south fork of Bulson Creek is joined by the north fork of Bulson Creek where they cross Bulson Road, pass by a dairy farm, and enter Hill Ditch.

Starbird Creek (Basin No. 8) upper reaches are heavily forested and undisturbed.  The north fork of Starbird Creek begins in a wetland north of Tyee Road and works its way south on the west side of the Pilchuck Tree Farm.  South of the Pilchuck Tree Farm, the north fork of Starbird Creek opens up into a pasture that is being over-run with reed canary grass and is very wet in nature.  The stream then crosses Starbird Road where it is joined by one of the middle forks of Starbird Creek.

The middle forks of Starbird Creek begin one mile west of Lake McMurray and travel west through a heavily forested area.  The southern stem of the middle fork of Starbird Creek crosses the road at the corner of Starbird Road and English Grade Road.  The stream at this location drains a small ravine and has good overall habitat values with a bank full width of 5 feet, a bank full depth of 8 inches with a gravel bed. Traveling west, the stream connects with the north fork of Starbird Creek downstream of this location.

The middle and north forks of Starbird Creek travel south in the sub-watershed where they cross Fremali Lane.  The stream at Fremali Lane contains a bank full width of 12 feet, a bank full depth of 3 feet with a narrow buffer of alder and spirea.  Further downstream, Starbird Creek crosses Starbird Creek Lane and Bulson Road.  Both Fremali Lane and Starbird Creek Lane are in residential developments that have resulted in rerouting of the channel. Starbird Creek at Bulson Road has gravel bars and large cedar trees to shade the stream.  West of Bulson Road, Starbird Creek meets up with Big Fisher Creek.

The south fork of Starbird Creek begins one-half mile east of English Road and flows into a forested wetland and then crosses Starbrook Lane.  After Starbrook Lane, the south tributary of Starbird Creek enters another forested wetland.  Field observations made during this study could not identify the exact location where the south fork of Starbird Creek enters the main stem of Starbird Creek, but it is believed to flow in on the south end of Fremali Lane and connect to Starbird Creek before Starbird Creek Lane.

Big Fisher Creek (Basin No. 9) upper reaches are heavily forested and undisturbed.  The north fork Big Fisher Creek begins approximately one mile south west of Lake McMurray and travels south west through an established forested area and crosses 324th Street NW, where there is a nearby pond.  The stream at this location is eroding at the bank.  The north fork of Big Fisher Creek continues southwest where it joins with middle and south forks of Big Fisher Creek.

The middle fork of Big Fisher Creek begins approximately one half mile south of the north fork to Big Fisher Creek.  It begins in a forested area and flows southwest where it crosses English Grade Road and flows into the southern fork of Big Fisher Creek.  The creek at the English Grade Road location has a gravel and cobble bed and is contained in a ravine with mature cedar riparian buffer.    From this location, the creek continues in a southwesterly flow and crosses 324th Street NW where there is a man-made pond that just to the west of the creek.  Southwest of this location, the middle fork of Big Fisher Creek flows into the south fork of Big Fisher.

The southern-most fork of Big Fisher Creek begins approximately one half mile south of the middle fork of Big Fisher Creek and flows northwest before flowing west.  The first major crossing of the southern fork of Big Fisher Creek occurs on 24th Avenue NW.  The creek at this location is contained in a small ravine with a natural ledge creek bed surrounded by mature cedar trees.  After this location, the stream enters a pasture before crossing English Grade Road.  It then enters a pasture that has minimal riparian vegetation and an animal access for a short distance before entering into a deciduous forest and combining with the middle fork of Big Fisher Creek.

After combining with the middle fork, Big Fisher Creek flows west where it is joined by the north fork of Big Fisher Creek.  Together, these creeks cross 324th Street NW, where the stream begins an approximate one-mile stretch of water that borders residential homes, pastures, and a pipeline easement, crossing 44th Avenue and Starbird Road.  In this area, technicians noted bank trampling, straightening of the creek in pasture areas, and ditching of the stream.  Further down from Starbird Road, the creek enters anarea with a well established riparian area.  The bed is gravel, and there is large woody debris in the creek forming pools down to Cedardale Road.  At Cedardale Road, the bank full width of the stream is 30 feet, the bank full depth is 3 feet, and the flood plain is 50 feet wide.  From Cedardale Road, Big Fisher Creek passes through a fish ladder and travels under Interstate 5 where it passes by a junkyard, a deciduous forest, and enters the Hill Ditch system.

Upper reaches of the Little Fisher Creek (Basin No. 10) Both the east fork and the west fork of Little Fisher Creek, begin in naturally occurring wetland and travel north through small forests, small farms, and around homes.

The west fork of Little Fisher Creek has an 8-foot bank full width as it crosses 324th Street NW and goes through a forested wetland.  As the creek continues north, it crosses the Snohomish/Skagit County line, and encounters a small concrete dam that is retaining approximately 8 feet of water.  The west fork of Little Fisher Creek continues north through a deciduous forest to Milltown Road. After Milltown Road, the creek passes through multiple driveways and lawns, where it enters a cattle pasture and departs into the Hill Ditch system at Fisher Slough.

The east fork of Little Fisher Creek is an extensive vegetated wetland with cedar, spirea, and salmonberry. It crosses 324th Street NW and travels north to the County Line Road.  It then reaches the Brunn Road where it travels through several yards in a residential subdivision.  From Brunn Road, the east fork of Little Fisher Creek crosses Pacific Highway South and is joined by an unnamed tributary that crosses under I-5.  The east fork of Little Fisher then flows under Milltown Road at the I-5 overpass and goes under Bonnie View Road.  After Bonnie View Road, the stream enters a vegetated zone with a mature cedar trees.  After crossing under Franklin Road, the east fork of Little Fisher Creek combines with the west fork of Fisher Creek and continue to flow north where they meet with up with the Hill Ditch system in Fisher Slough.

Sloughs

Fisher Slough was not in the planning scope for this characterization, but has been well documented in the Nature Conservancy’s Fisher Slough Study (Tetra Tech, 2006).

Man-Made Channels

Hill Ditch

Hill Ditch was created in the early 1900’s to channel the water from Stackpole, Carpenter, Lake Ten, Sandy, Johnson, and Bulson Creeks into the original mouth of Fisher Creek.  This project was originally routed through the town of Conway.  During the 1930’s, local landowners and the diking district extended Hill Ditch south to Fisher Creek, complete with11-foot high dikes on both sides of the slough, and manual tide gates at the mouth that act as large barn doors that can close in the event of a high water on the Skagit River.  In and around this time period, the Works Progress Administration (WPA) created the “siphon” (aquaduct underpass) on Fisher Slough that enabled the water of Maddox Creek in south Mount Vernon to pass underneath Fisher Slough and drain into Skagit Bay; this system is referred to as Big Ditch.  These two massive diking and drainage projects enabled farmers to farm the productive soils of the Conway area with a reduced chance of flooding to their fields and resulted in a system of dikes well over 25,000 feet in over-all length that still function to this day.

Throughout its history, Hill Ditch has been perceived to be a man-made structure and was dredged routinely by the local diking and drainage district until recent years.  Currently, the Hill Ditch system is over-run with reed canary grass (Phalaris arundinacea) and filled with sediment.  The main source of sedimentation in Hill Ditch on the flats is soil eroded from forested land logged approximately 20 years ago on highly erodible banks, combined with beaver dams giving out in the head waters sending a rush of water downstream.  During wet weather conditions, plumes of highly turbid water and gravel can frequently be seen flowing into Hill Ditch from smaller creeks such as Johnson Creek.  Conversely, the outflows from Carpenter Creek tend to have visibly lower turbidity, due to the high quality riparian habitat and stream slope.

## Wetlands

Wetlands have important hydrologic and wildlife habitat functions.  Hydrologic functions include storing precipitation and runoff and then releasing it gradually.  In this way, peak runoff flows in the upland tributaries and the slough are attenuated.  Likewise, flow in the tributaries is extended further into the summer dry season than it otherwise would be. Wetlands also can serve as areas of groundwater recharge, provided that the underlying soil is permeable enough.  In the Fisher/Carpenter Creek Watershed, the low permeability of the soil probably limits groundwater recharge (see Chapter 5).  Habitat functions include breeding areas for amphibians and cover for birds, mammals, and other animals.

In the Fisher/Carpenter Creek Watershed, the National Wetland Inventory lists 93 wetland areas that are particularly valuable due to either their large size and/or their habitat quality.  In the northern half of the watershed that includes Sandy, English, Carpenter, Lake Ten, and Johnson Creeks (sub-basins 1-6), the wetlands are largely listed as palustrine, forested, scrub-shrub, and emergent.  In the southern half of the watershed that includes Bulson, English and Fisher Creeks (sub basins 7-10), are several large palustrine, forested, scrub-shrub, and emergent wetlands.  The size and distribution of these wetlands in the southern watershed appear to be larger and more widespread.  These wetlands store a large quantity of runoff and release it more gradually than runoff from the surrounding non-wetland areas.  These were not field-checked during the present study, however, they also appear to play a significant role in attenuating runoff from the watershed.

Figure 6.4 shows wetland locations within the Fisher/Carpenter Creek Watershed that are listed on the National Wetland Inventory.  In general, the National Wetland Inventory sites have not been formally delineated as jurisdictional wetlands, so their inclusion in Figure 6.4 is for general information purposes only.

Figure 6.5 Wetlands in the Fisher/Carpenter Creek Watershed

## 6.6	Key Hydrologic Structures and Fish Passage Blockages

During the period from December to June 2005, the Fisher/Carpenter Creek project team performed a field inventory of stream conditions and structures in the Fisher/Carpenter Watershed.  This inventory, listed in Appendix 3, describes various major fish passage blockages on Stackpole, Carpenter, English, Lake Ten, Johnson, Bulson, Starbird, and Fisher Creeks, including natural occurring waterfalls and unnatural culverts and dams as well as other hydrologic features such as areas of erosion, flood prone areas, channel structure etc.  Each creek varies in its hydrologic features, however all of them have at least one fish passage barrier and numerous perched outlets.  For detailed field notes, please refer to Appendix 3.

# 7	Water Quality

The intent of the Skagit Conservation District’s (SCD) Fisher/Carpenter Basin water quality monitoring program was to locate sampling stations along Fisher and Carpenter Creeks and their tributaries to show trends over time, both diurnally and seasonally.  Water quality data from the program has been described by parameter (fecal coliform, temperature, etc.) by discussing these changes.  The ultimate goal of the project is to protect, restore, and enhance water quality and fish and wildlife beneficial uses in the Fisher/Carpenter Basin.

Background

As a result of the Department of Ecology’s (DOE) 303d listing, the DOE has been addressing fecal coliform bacteria and temperature impairments in Carpenter/Fisher Creeks through the Total Maximum Daily Load (TMDL) process. The DOE is in the process of establishing a TMDL for fecal coliform in the Lower Skagit River Basin, which will include load allocations for the Fisher/Carpenter Basins (Butkus, 2000).  The DOE has also completed a technical study as part of developing a temperature TMDL for Skagit River tributaries, which will include load allocations for Carpenter and Fisher Creeks (DOE, 2004).

Besides agriculture, non-point sources to the drainage include urban development, surface mining (gravel extraction), and forestry practices.  Urban intensification, unstable slopes, and septic systems in unsuitable soils are probable causes for increased runoff from upland areas resulting in water quality degradation.  These impacts affect aquatic resources before they reach the flood plain, which is intensely diked and drained (Skagit County Public Works, 1997).

A series of surveys were conducted in 1994 and 1995 by the DOE as part of the Lower Skagit TMDL study.  Analysis showed widespread elevated levels of fecal coliform bacteria, temperature, and turbidity in several tributaries, including the Fisher/Carpenter basin. (Pickett, November 1996).  While the results of Dissolved Oxygen (DO) sampling met the Water Quality Standards throughout the lower Skagit River, additional investigation in the tributary reaches was warranted after the data went through the quality assurance phase.

Other than areas within the city limits of Mount Vernon that are serviced through the municipal sewer system, residents rely on septic systems for their sewage treatment.  Several small farm operations, including llamas, horses, sheep, and alpacas pose a potential threat to waterways due to poor waste management practices or by allowing uncontrolled animal access to waterways.   Commercial operations include one dairy and many small scale cattle (non-confined) operations.

## Water Quality Standards

All surface waters in the Fisher/Carpenter Creek watershed are considered “surface waters of the State of Washington.”   State water quality standards apply both to natural streams and ditched channels (Washington State 1997, Washington State Attorney General 1969). The Washington Class A Freshwater criterion applies throughout the Fisher/Carpenter watershed (Washington State 1992, WAC 173-201A-030). Characteristic uses for Class A waters are water supply, stock watering, fish rearing and spawning, wildlife habitat, recreation, and commerce. Selected water quality parameters and criteria are presented in Table 7.1.

Table 7.1 Selected Washington State Class A water quality

parameters and criteria (Washington State 1997).

| Parameter | Class A Freshwater |
| --- | --- |
| Fecal coliform organisms | Not to exceed geometric mean of 100 colonies per 100/ml; no more than 10% of samples may exceed 200 colonies per 100/ml |
| Dissolved oxygen | Shall exceed 8.0 mg/l |
| Temperature | Shall not exceed 18.0°C due to human activities |
| Turbidity | Shall not exceed 10% over natural background turbidity |

## 7.2 	SCD’s In-House Water Quality Monitoring Program

Since October of 2004, the Skagit Conservation District has been monitoring twelve sites in the Fisher/Carpenter basin for standard water quality parameters including temperature, dissolved oxygen, turbidity, and fecal coliform.  The original monitoring plan called for a bi-weekly sampling schedule.  The requirement for the samples to be analyzed at an accredited lab (Skagit County Health Department) rather than at the DOE Padilla Bay facility, necessitated a change in schedule to once per month to fit the cost into the grant budget.

Objectives

In order to identify and prioritize strategies for restoration and enhancement, a quantitative analysis of parameters has been undertaken at specific locations within the watershed.  Over the course of the study, the Skagit Conservation District has monitored the water quality at specific sites within the upper Carpenter basin.  The results were combined with available historical data, information from the ongoing Skagit County Public Works Monitoring Program, and findings from the Fisher/Carpenter Stream Team Monitoring Program that was designed and implemented by the Skagit Conservation District in the fall of 2005.

Sites

The Monitoring Program focuses on non-point source pollution parameters within the Fisher/Carpenter watershed.  Sites on the main stem of Carpenter Creek and tributary reaches have been selected to address site-specific water quality issues.  The list below consists of site numbers, the WRIA identification for the streams to be sampled, and stream miles where applicable.

- Fisher Creek WRIA 0181

  - Site 1-BRFC -Fisher Creek Fisher Creek SM 3.08

  - Site 2-FRFC-Fisher Creek at Franklin Road Skagit County Public Works site #48. SM1.3

- Lower Carpenter-WRIA #3.0179  (Carpenter Creek and tributary inputs)

  - Site 3-16BC-Bulson Creek WRIA #3.0198-upstream Bulson Creek on Sixteen Lake Road

  - Site 4-BCBR-Bulson Creek on Bulson Road upstream of a dairy farm

  - Site 5-DBCC-Carpenter Creek (Hill Ditch) at the downstream boundary of the dairy farm. Approximately SM 2.5

  - Site 6-CEBC-Culvert east of the dairy (input to) SM2.9LB

  - Site 7-UBCC-Carpenter Creek (Hill Ditch) upstream of the dairy farm. Approximately SM 3.1

  - Site 8-CHCC-Carpenter Creek (Hill Ditch) Conway Hill bridge at SM 2.0

  - Site 9-UMJC-Johnson Creek WRIA #3.0204 enters Carpenter Creek (Hill Ditch) at SM 3.55LB.

  - Site 10-UMSC-Sandy Creek WRIA #3.0205 enters Carpenter Creek (Hill Ditch) at SM 4.7 LB.

  - Site 11-UM10-Ten Lake Creek WRIA #3.0207 enters Carpenter Creek (Hill Ditch) at approximately SM 5.6 LB.

  - Site 12-GPCC-Carpenter Creek below Gravel Pit on Hickox Road SM 6.4 LB

Figure 7.2 – Sampling Sites – Circles 1-12 SCD In-House.

Triangles 1-4 Stream Team

## 7.3	SCD’s Stream Team Citizen Water Quality Monitoring

Objectives

The primary objectives of the Stream Team program are:

- To inspire community stewardship in regards to water quality by educating local citizens about land use and non point sources of pollution by involving them in the process of water quality data gathering.

- To develop and implement a routine sampling program that can be used to assess water quality trends, to characterize existing water quality of priority freshwater drainages, and to determine if water quality within the study area meets Washington State Water Quality Standards.

- To document improvements in water quality as a result of the implementation of Best Management Practices on farmlands and the repair and/or replacement of failing septic systems.

- To teach community volunteers the sampling and analytical techniques used by environmental professionals, how to manage the data collected and create a database, and the importance of establishing a long-term water quality monitoring program.

- Information and data collected can be used as supplemental information to identify problems, possible sources of pollution, and potential solutions.

Sites

  - Site 1-Big Fisher Creek – WRIA 3.0181 on Bulson Road - furthest upstream

  - Site 2-Big Fisher Creek off Bulson Road – Boulton/Briggs property – access by permission

  - Site 3-Big Fisher Creek on Starbird Hill Road

  - Site 4-Big Fisher Creek at Franklin Road SCD site #3 – also Skagit County Public Works site #48. SM1.3

## 7.4	Sources of Water Quality Degradation

There are no documented “point sources” of pollution in the Fisher/Carpenter Creek watershed. However, there are a variety of “non-point sources” of pollution in the watershed that could have the potential to degrade the water quality relative to the Class A freshwater Washington State Water Quality Criteria. In the uplands, non-point sources include stormwater runoff from roads and parking areas, areas where livestock congregate, manure storage areas, pet and wildlife waste, and run off from fertilizers, herbicides, and pesticides applied to both agricultural land and residential lawns and landscapes. Erosion resultant from unsound logging practices (prior to the Forest Practices Act RCW 76.09) and poorly functioning on-site septic systems are also believed to be a significant non-point source of pollutants. Blocking culverts and other obstructions impound water and reduce stream flow (SRSC, 2001).  The increase in impermeable surfaces in the watershed due to road building and home construction is likely partially responsible for reduced recharging of the aquifers and increased volume in storm flow.

Looking at previous studies and the data collected in the SCD monitoring program, the following observations can be made regarding potential sources of degradation of selected water quality parameters in the Fisher/Carpenter Creek watershed.

Temperature

It is believed that elevated summer water temperatures in the streams and ditches in the basin are due to lack of vegetative cover, lack of surface water flow from the upland tributaries, and lack of groundwater inflow.  Loss of wetlands due to changes in land use is a likely contributor to the decrease in groundwater base flow.

Figure 7.31.  Temperature in º Celsius

Less than 2% of the samples exceeded the standard of no more than 18º C for temperature.  That is likely due to the time of day the samples were taken and the shading capability of reeds canary grass.

Dissolved Oxygen

The significant seasonal variability in dissolved oxygen in Carpenter Creek and its tributaries may be attributed to several potential factors. First, the very low summer base flow of water in the creek most likely consists mostly of phreatic inputs of groundwater, which is typically low in dissolved oxygen. Second, the elevated fecal coliform levels in some reaches suggest that it might be impacted by faulty on site septics as well as runoff from non-confined livestock areas and other non-point sources such as domestic pets and wildlife waste that typically have high nutrient concentrations. As bacteria in the creek metabolize the nutrients, they consume dissolved oxygen and decrease the oxygen concentration in the water.  Third, the removal of shading vegetation and its cooling effect along the stream systems increases the water temperature, decreasing the solubility of oxygen in the water.

Figure 7.32  Dissolved oxygen in mg/L

Of the samples taken, 18% of the samples did not meet the minimum standard for dissolved oxygen levels. Nearly a quarter of those samples (24%) were taken at Site #7, UBCC (Upstream Boon, Carpenter Creek/Hill Ditch).  There is no shade along this reach and the slope is very low.  Reeds canary grass is thick along the banks and in the streambed, further slowing the movement of the water.

Fecal Coliform

Without additional bracket sampling, no clear sources of fecal coliform contamination can be identified.  Potential sources include failing septic systems, uncontrolled animal access to streams, domestic pets, and wildlife.

Figure 7.33 Fecal coliform in cfu/100mL

Of the samples collected, 14% have been higher than the 100 colonies per milliliter allowed under state standards.  Site #1, BRFC (Bulson Road / Fisher Creek) had 24% of the exceeding levels.  This site is the furthest site upstream on Fisher Creek and is directly downstream of unrestricted cattle and horse access to the stream.  Upstream of the site is open pasture, with no shade available to the stream.  Of the remaining samples in excess of the standards, was at site 4 – CEBC (Culvert East / Bulson Creek), site 5 – DBCC (Downstream Boon - Carpenter Creek / Hill Ditch), site 6 – CNBR (Culvert North Bulson Road), and at site 12 – GPCC (below Gravel Pit – Carpenter Creek).  Twice at Site 1, three of the high levels were recorded on the same day (November12, 2004 and August 12, 2005), following sustained heavy rain.

Turbidity

The potential sources of particulates and suspended sediment that contribute to turbidity in Fisher/Carpenter Creek include runoff from roads and other impervious surfaces, erosion of ditches and channel banks, erosion resultant from poor logging practices, and re-suspension of trapped particles and sediments during periods of high flow.

Figure 7.34 Turbidity in NTUs

Spikes in turbidity occurred at Site 9 – UMJC (Upstream Mouth Johnson Creek), following periods of sustained heavy rain.  The 148 NTU reading at Site 9 on November 9, 2004, the entire county was under a flood watch. This reach of Johnson Creek has several issues that impact the stream and the surrounding property.  In portions of it, the stream is actually higher than the roadbed.  At times of high flow, the stream breaches its channel then flows across the road prior to entering Carpenter Creek.  Beavers are active in the area, impounding water both upstream of the mouth of Johnson Creek on Carpenter Creek and within Johnson Creek, reducing the flow.  During periods of low flow, Johnson Creek is often reduced to little more than a trickle.

## 7.5	Quality Assurance / Quality Control

As mentioned earlier, the original plan of bi-weekly sampling was changed to once per month due to budget constraints.  The cost of having the Fecal Coliform samples analyzed by an accredited lab (Skagit County Health Department rather than the facility at the Padilla Bay Research Reserve) was the driving factor.

pH was dropped from the plan as the borrowed meter was inaccurate and unable to be calibrated.  There were no funds available for a replacement.

There was one sampling date (February 15, 2005) when the turbidity levels were omitted from the results, due to faulty readings (false highs) on the Turbidimeter.  The batteries were changed in the meter and it was re-calibrated prior to further use.

All water samples were obtained using clean (boiled) nalgene bottles, except for fecal coliform sampling, which was collected in sterilized/sealed bottles provided by the Skagit County Health Department.  Collected coliform samples were stored on ice prior to delivery to the Skagit County Health Department.  Samples were delivered within six hours of collection and analysis was begun the same day of collection.

Duplicate fecal coliform samples were taken at a rate of 20% throughout the length of the study.  As seen in other water quality studies, such as the ongoing Skagit County Public Works Monitoring Program, there was variability in results due to erratic loading that occurs naturally in stream systems.  The Winkler method for dissolved oxygen levels were run at a 10% rate.  Results were compared and showed consistently to be within a .3 mg/L range.  Dissolved oxygen levels were also cross-checked by using two different YSI meters at the same time, with like results.

Two stream reaches were characterized according to USDA/NRCS specifications from Technical Note 99-1, Stream Visual Assessment Protocol (USDA 1998).  They were at the Franklin Road site as a reference reach and along Johnson Creek.  The Johnson Creek site is highly impaired by land use and road building.  During periods of high flows, the creek tends to “blow out” of its channel, carrying high loads of sediment and gravels into the Carpenter Creek system.  The reach has been targeted for restoration and enhancement by Skagit County Public Works.

Data collected was entered into the Skagit CD’s database and is currently being entered into the Department of Ecology’s Environmental Information System, as directed in the Fisher/Carpenter TMDL Implementation Grant.  The spreadsheets were meticulously reviewed for accuracy by comparing field sheets with the database.  Errors in decimal placement were corrected prior to statistical analysis.

Comparisons of results obtained during the period of October 2005 and June 2006 by the Skagit Conservation District (SCD), Skagit County Public Works (SCPW), and the Skagit Stream Team (ST) were made at the Franklin Road site.  When possible, samples for SCD and SCPW were gathered simultaneously, using an Ecology approved collection bucket as split samples.  Variations in results with the Stream Team are likely due to the time of day or the day itself the samples were obtained.  Results used for comparison were chosen from the samples collected closest to the date of the SCD sampling.  The Stream Team also employs the membrane filtration for fecal coliform analysis while the SCD and SCPW samples were analyzed by the Most Probable Number (MPN) method at the Skagit County Health Department water lab.

Figure 7.41 Comparison of results for dissolved oxygen in mg/L between the

Skagit Conservation District (SCD), Skagit County Public Works (SCPW), and The Stream Team (ST) between October 2005 and June 2006 at the Franklin Road site.

Figure 7.42 Comparison of results for temperature in º Celsius between the

Skagit Conservation District (SCD), Skagit County Public Works (SCPW), and The Stream Team (ST) between October 2005 and June 2006 at the Franklin Road site.

Figure 7.43 Comparison of results for fecal coliform as cfu/100mL between the Skagit Conservation District (SCD), Skagit County Public Works (SCPW), and The Stream Team (ST) between October 2005 and June 2006 at the Franklin Road site.

# 8	Fish and Wildlife Habitat

An inventory of common plant and animal species, and evaluation of habitat function and value for the Fisher/Carpenter Creek Watershed is described in the following paragraphs.  The various habitats include undeveloped areas shown in Figure 3.3 and upland wetlands shown in Figure 6.4.  Remaining forested areas consist of second-growth Douglas fir, Western red cedar, and various hardwoods.  In the late 1800s, the pasture areas were created by pulling and burning stumps in logged areas.  Pastures today contain a mixture of pasture grasses, native grasses, and invasive grasses and herbs.  As discussed in Chapter 6.4, wetlands occur in both pasture and forested areas where the hydrology and soil conditions retain surface runoff.

## 8.1	Species Inventory

Vegetation

Native vegetation in the Fisher/Carpenter Basin is formed of fairly young seral stands dominated by Douglas firand Western red cedar, and is fairly indicative of post-logging second growth forest conditions in the western hemlock zones of western Washington and northwestern Oregon (Franklin and Dyrness, 1973).

Hardwoods are not common in the upland forested areas but are often seen in recently disturbed locations and riparian areas.  In these conditions, red alder and big leaf maple are most prevalent.  Understory plant communities, supported by the wet, mild, maritime climate of this zone, are mostly composed of Indian plum, red osier dogwood, vine maple, and various willow and rose species. Groundcovers commonly found within the basin are ferns, salal, and kinnikinnick.  Common wetland species include skunk cabbage, small-fruited bulrush, ninebark, twinberry and cattails.

Invasive exotics such as reed canary grass and Himalayan blackberry are found throughout the basin and are extremely abundant along the lower portions of both Fisher and Carpenter Creeks, nearly to the exclusion of any other species in some areas.

Wetland Heritage

There are two locations within the northeast portion of the watershed identified by the Natural Wetland Heritage for the existence of rare specie and/or because of a high quality wetland ecosystem (NWI, 2005).  Neither location is easily accessible to the public and is in the heavily forested area upland of the headwaters of Sandy and Johnson Creeks.  The Heritage survey ranks both sites as “Sensitive” which means that it houses a living thing that is vulnerable or declining in number and/or health and could become endangered or threatened in the state if efforts aren’t made to actively remove threats.   The species listed include Bristly sedge, Low elevation sphagnum bog species, Western hemlock, and Western Red cedar.

## 8.2	Evaluation of Habitat Quality

The upper reaches of Sub-basins 3,4,5,6,7,8 and 9 (Figure 6.1) contain large expanses of industrial forestlands.  These forestlands provide habitat for such mammals as deer.  Some reaches historically, and to a more limited extent today, provide habitat for salmonids.  While the pasture areas primarily serve for cattle grazing and growing hay in this area, isolated thickets of wild rose and other shrubs offer cover for songbirds and mammals like raccoon and deer.  There are large areas of pasture, particularly in Sub-basin 7, 8, 9, and 10, and the southern part of Fisher/Carpenter Creek Watershed.  Residential housing development is gradually fragmenting pasture habitat in other sub-basins.  Historic ditching affects the hydrology of the pasture areas, which has most likely reduced the overall area of upland wetland that occurred prior to settlement in the 19th Century.

Habitat quality in forested areas is gradually improving as the second growth forests mature.  Particularly good habitat exists in Sub-basin 3 and 5, where isolated stands of very large (possibly old-growth) fir and cedar have been noted, and in the upper reaches of Sub-basins 7, 8, and 9.  Smaller woodlots in other sub-basins are more fragmented, but still provide some habitat value, as many of them contain forested wetlands.  Due to wetland protection designations in the Washington Growth Management Act, it is probable that habitat conditions in at least some of these smaller woodlots will continue to improve over time, even as the surrounding upland pastures are more intensively developed.

Sub-basin 1 (Stackpole Creek) has little habitat value for fish.  There are essentially no riffles or pools, large woody debris, side channels, or other structural features that would provide habitat value.  Because dredging has deepened the creek it is disconnected from its floodplain.  Several drainage and roadside ditches feed into the reach, which results in a sharply peaked hydrograph pattern, and the reach typically runs dry in the summer.

In the English, Carpenter, Lake Ten, Sandy, Johnson, Bulson, Starbird, Big Fisher, and Little Fisher Creeks sub-basins, creek channels and adjacent riparian areas contain fish habitat features of varying function.  Features such as riffle and pool channel morphology, large woody debris in the channel, undercut banks, and diverse, mature communities of riparian vegetation are present throughout the three sub-basins.  In general, the frequency and quality of these features decreases in relation to an increase in development, with the highest quality fish habitat present in the areas relatively inaccessible to the public.

The Hill Ditch system is the main detractor of overall good quality fish habitat within these reaches.  It is a diked and dredged channel that is disconnected from the floodplain because of the levee system keeping the stream within its banks over a distance of approximately 25,000 feet. This diked condition precludes the development of side channels, which act as “refuges” for fish during seasonal high water flows.

A second condition that detracts from the fish habitat quality is the sharply peaked runoff hydrograph that characterizes flow in Hill Ditch.  Due to deforestation and extensive ditching along roads and in pastures in upstream areas, runoff drains very rapidly.  The resulting high flow velocities erode the banks and put stress on fish and aquatic invertebrate utilization of the creek. The peaked hydrograph also results in extreme dewatering of the channel during the dry season.

The third major negative habitat impact in Hill Ditch is perched, buried, undersized, and/or blocking culverts.  Sub-basins 1, 2, 3, 4, 7, 8, 9 and 10 all have one or more culvert issues that impact fish habitat.  Appendix 3 contains an inventory and description of these culverts.

## 8.3	Endangered Species Act

Appendix 7 shows listed and proposed endangered and threatened species that the United States Department of Fish and Wildlife has identified in Skagit County.  Of these, the species that are most likely to be found in the Fisher/Carpenter Watershed are the Bald Eagle and the Lamprey.  In addition, Puget Sound Coho, a candidate species, has also been observed in both Fisher and Carpenter Creeks.

References

Literature Cited

Aitkin, J.K. 1998. The Importance of Estuarine Habitats to Anadromous Salmonids of the Pacific Northwest:  a Literature Review.  US Fish and Wildlife Service: Lacey, Washington.

Beamer, E., A. McBride, R. Henderson, and K. Wolf. 2003. The Importance of neo-natal Pocket Estuaries in Skagit Bay to Wild Chinook Salmon:  An Emerging Priority for Restoration.

Butkus, Steve, D. Pater, P. Pickett, 2000.  Lower Skagit River Fecal Coliform Total Maximum Daily Load.  Washington State Department of Ecology, Olympia, Washington. Publication No. 00-10-010.

Collins, B. D. and Sheikh, A. J. 2003. Historical Aquatic Habitat in River Valleys and Estuaries of the Nooksack, Skagit, Stillaguamish, and Snohomish Watersheds, May 1, 2003.  Report to Northwest Fisheries Science Center, National Marine Fisheries Service, P.O. Box 157, 2725 Montlake Blvd. E., Seattle, WA  98112.

Cotterill G. F. The Climax of a World Quest (Seattle: Olympic Publishing Company, 1928), 170-74, 180-81, 183-84.

Entranco, 1991. Lower Skagit Basin Water Quality Study Analysis of Historical

Water Quality Data.  Entranco, Bellevue, WA

Entranco, 1993. Lower Skagit River Basin Water Quality Study Final Report.  Prepared by Entranco, Bellevue, WA.  Revised and Edited by Skagit County Department of Planning and Community Development, Mount Vernon, WA.

Franklin, J. F. and C. T. Dyrness.  Natural Vegetation of Oregon and Washington.

Oregon State University Press.

Jantz, D. Personal Interview, Issues of Putting in a Well.  April 5th 2005.

Knapp, R.E.L. 1933. Road Map Skagit Co. Washington Prepared for Skagit County, Washington. Mount Vernon, WA.

Leonard, Budinot, and Skodje. 1998.  Skagit County Culvert Evaluations Fish Passage Improvement (Task No. 1) Prepared for Skagit County, Washington. Mount Vernon, WA.

Marshal R.B. Topography of the State of Washington, 1911.

Maynard, D.N. and G.J. Hochmuth. 1997. Knott’s Handbook for Vegetable Growers, Fourth Edition.  John Wiley and Sons, Inc.:  New York.

Meany, E. S. Vancouver’s Discovery of Puget Sound (Portland, OR: Binfords & Mort, 1957), 125-26, 148, 158, 161-66, 169, 174-75, 178.

Oldham, K, Joseph Whidbey Circumnavigates Whidbey Island in June, 1792 (historylink.org January 17, 2003) 1-2.

Pickett, P.J., 1997.  Lower Skagit River Total Maximum Daily Load Water Quality   Study.  Environmental Investigations and Laboratory Services Program.

Washington State Department of Ecology, Olympia, WA.

Pitz, C.F. and Robert S. Garrigues. 2000.  Summary of Streamflow Conditions, September 2000: Fisher Creek and Carpenter Creek Basin.  Washington State Department of Ecology.

Reiser, D.W. and T.C. Bjornn. 1979.  Habitat Requirements of Anadromous Salmonids. In: W.R. Meehan, Editor, Influence of Forest and Rangeland Management on Anadromous Fish Habitat in Western North America. U.S Forest Service General Technical Report PNW-96. Pacific Northwest Forest and Range Experiment Station, Portland, Oregon.

Schuler, T. 1994.  The Importance of Imperviousness.  Watershed Protection Techniques 1(3): 100-111.

Seitz, R.C. W.R. Chenowth, A.J. Bauska, and B.F. Martin, U.S. Department of the Army Corps of Engineers.  U.S. Department of the Interior Geological Survey.  1940 topographic map.

Skagit Conservation District and Washington State Department of Ecology, Padilla Bay National Estuarine Research Reserve.  No Name Slough, Skagit County, Washington:  Watershed Characterization. : Mount Vernon, Washington.  90 pp plus appendices. [Washington State Department of Ecology Publication No. 04-06-017.]

Skagit County Historical Museum.  New Map of the Puget Sound County Fifth Revised Edition 1903, Road Map Skagit Co.

Skagit County, 2004.  Skagit County Monitoring Program Annual Report 2004. 2004 Water Year (October 2003 – September 2004).  Rick Haley, Mount Vernon, Washington.

Skagit County Department of Planning and Community Development, 1988.  Skagit County Watershed Ranking Project.  Skagit County Department of Planning and Community Development:  Mount Vernon, Washington.

Skagit River Systems Cooperative, 2001.  Skagit County Culvert Assessment.  SRSC, LaConner.

Soil Conservation Service, United States Department of Agriculture, 1989.  Soil survey of Skagit County area, Washington. 372 pp. [In cooperation with Washington State Department of Natural Resources and Washington State University, Agriculture Research Center.] United States Department of Agriculture, Soil Conservation Service.

Soil Conservation Service, United States Department of Agriculture, 1983.  Soil survey of Snohomish County area, Washington. 197 pp.  United States Department of Agriculture, Soil Conservation Service.

Tetra Tech Inc., 2006.  Fisher Slough Hydrodynamic Assessment and Restoration Design.

U.S. Department of Agriculture Commodity Stabilization Service, Skagit County, WA, 1957, sheet 5.

Washington State. 18 November, 1997. Washington Administrative Code, Chapter 173-201A WAC, Water Quality Standards for Surface Waters of the State of Washington. 18 pp. Washington State: Olympia, Washington.

Washington State Attorney General, 1969. Attorney General Opinion, 1969 No. 4: Opinion given to James P. Behlke, Director, Water Pollution Control Commission. 10 pp. Olympia, Washington. [to be cited as AGO 1969 No. 4]

Washington State Department of Ecology (WDOE) well log site, http://apps.ecy.wa.gov/welllog/sitei.asp

Washington State Department of Ecology (WDOE), 2004.  Lower Skagit River Tributaries Temperature Total Maximum Daily Load Study.  Publication No. 04-03-001.

Washington State Department of Ecology (WDOW), 2000. Summary of Streamflow Conditions, Fisher and Carpenter Creek Basin, September 2000. http://www.ecy.wa.gov.biblio/0003049

Washington State Department of Fish and Wildlife, 1983.  Skagit County Stream Assessment.  Rich Johnson, LaConner, WA.

Washington State Department of Natural Resources, 2005.  National Wetland Inventory, Personal communication with Sandra Moody, Sandra moody@wadnr.gov.

Washington State Department of Transportation, 1997. Hydraulics Manual, 2003.

Weinmann, F., M. Boule, K. Brunner, J. Malek and V. Yoshino. 1984. Wetland Plants of the Pacific Northwest. 85 pp. [Prepared for U.S. Army Corps of Engineers, Seattle District]. Seattle, Washington.

Weisberg, S. and Riedel, J. 1991. From the Mountains to the Sea:  A Guide to the Skagit River Watershed.  North Cascades Institute:  Sedro-Woolley, Washington.

Map Source:  Joe Holtcamp, Skagit Conservation District.  CREP/GIS Coordinator.  joe@skagitcd.org

# Appendices

Appendix 1: Field Data

Fisher Carpenter Watershed Survey of Hydrologic Features

| Sub-basin Name: Stackpole Creek |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Stackpole 01 | E. Hickox Rd | ? | 12" rcc road crossing culvert | Collects roadside runoff from Sahale and E Hickox Rds. Outlets to a dtich, |
|  |  |  |  |  |  | Outlet perched 3'. |  |  |  |  |  |
| Stackpole 02 | E Hickox Rd | ? | Field ditch |  |  | Eroded field ditch thru pasture down hillside to Stackpole Creek. No buffer |
| Stackpole 03 | E Hickox Rd | P95582 | 18" rcc road crossing culvert | Opposite # 20231 E. Hickox. Collects runoff from Pamela Road to divide east of |
|  |  |  |  |  |  | Sahale Road. Outlets to ditch. Outlet perched 1'. |  |  |
| Stackpole 04 | E Hickox Rd | P16265 | Field ditch |  |  | Ditch through pasture to Stackpole Creek. No buffer. |  |  |
| Stackpole 05 | Stackpole Rd | P16257 | 18" road crossing culvert | Stackpole Creek U.S. is ditch thru canary grass pasture. DS 6' wide x 4' deep |
|  |  |  |  |  |  | ditch lined with knotweed |  |  |  |  |
| Sub-basin Name: Lake Ten Creek |  |  |  |  |  |  |  |  |  |  |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Lake Ten 01 | Casc. Ridge Dr. | P16603 | Lake outlet, 36" CPP culvert | Outlet of Lake 10 is small. New culvert under unpaved access road, not perched. |
|  |  |  |  |  |  | Entire mountainside is logged, but required riparian buffer along creek seems ok. |
| Lake Ten 02 | Casc. Ridge Dr. | P107271 | 48" CPM road crossing culvert | Creek channel in OK shape. Outlet perched 1'. Narrow tree buffer (and some |
|  |  |  |  |  |  | slash) on F/P, but not a big problem |  |  |  |
| Lake Ten 03 | Grouse Drive | P83858 | 48" CMP road crossing culvert | About 60' long, outlet perched 1'. Probably a complete fish passage barrier. |
| Lake Ten 04 | Casc. Ridge Dr. | P16253 | Confluence with Carp. Crk | About 150 u.s. of Casc. Ridge Dr. (not as shown on map). BFW 3', BFD 18". |
|  |  |  |  |  |  | Small flow 7/22/04. Decent forest cover, probably forested wetland on F/P. |
|  |  |  |  |  |  | Sand accumulation at mouth. No erosion. |  |  |  |
| Sub-basin Name: English Creek |  |  |  |  |  |  |  |  |  |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Engl. 01 | Casc. Ridge | P119686 | culvert crossing |  | Undetermined size CMP on "Alderbrook Lane,' area recently clearcut for future |
|  |  |  |  |  |  | residential development. Area will increase runoff to upper Carp. Crk when devel. |
| Engl. 02 | Ervine Rd | P16240 | 18" CPP road crossing culvert | Logging road, newly logged area. Small trib from west 5' BFW, 4" BFD drains |
|  |  |  |  |  |  | large salmonberry wetland. Confluence with Carp. Creek about 100' d.s. |
|  |  |  |  |  |  | The end of the logging road is 1.1 miles from Little Mountain Road jct. |  |
| Engl. 03 | Ervine Rd | P29743 | 30" RCC road crossing culvert | Outlet perched 2', small ravine Crk. BFW 11', BFD 12" medium gravel, not eroded |
| Engl. 04 | Ervine Rd | P29726? | 3' CMP road spur crossing culv. | Road spur off Ervine Rd. Outlet not perched. Crk BFW 12', BFD 1', gravel/small |
|  |  |  |  |  |  | cobble, erosion not a problem |  |  |  |  |
| Engl. 05 | Ervine Rd | P29738 | 4' CMP road crossing culvert | Unmapped trib from wetlands to SE. U.S. BFW 10', BFD 12", sand bed, salmon |
|  |  |  |  |  |  | berry, alder cedar. Outlet perched 17", 3' impassable rock drop below. Lots of |
|  |  |  |  |  |  | bank erosion/scour around outlet. Probably a fish passage barrier. |  |
| Engl. 06 | Ervine Rd | P29699 | 30" CMP road crossing culvert | Culvert on east trib. of Carp. Crk. Not perched, not eroded. SCD "Fish Stream" |
|  |  |  |  |  |  | sign. Creek DS of culvert BFW 12', BFD 18", gravel/cobble bed. Good riparian |
|  |  |  |  |  |  | cover of skunk cabbage, salmonberry, vine maple, alder. |  |  |
| Engl. 07 | Driveway | P101277? | ? |  |  | Unknown crossing. No culvert or bridge located: no access to private land |
| Sub-basin Name: Carpenter Creek |  |  |  |  |  |  |  |  |  |
| Carp. 01 | Gaspard Ln | P29797 | 12' x 12' bridge road crossing | Creosote timber bridge. Channel under bridge armored, BFW 5', BFD 18" |
|  |  |  |  |  |  | PEME wetland downstream. U.S. salmonberry (PSS wetland?) floodplain |
| Carp. 02 | Little Mtn Rd | P29781 | 18" RC road crossing culvert | Small trib from north crossing LM Rd, narrow alder and blackberry buffer |
| Carp. 03 | Little Mtn Rd | P29706 | 18" CMP road crossing culvert | Small drainage from wet area/blueberry fields north of LM road. (not mapped) |
| Carp. 04 | Little Mtn Rd | P101277 | ? |  |  | Unknown driveway crossing - not located because no access to land |  |
| Carp. 5 | Eaglemont Dr. | P104336 | Golf course - headwaters | Eaglemont golf course is the headwater of north trib. Extensive filling of wetlands |
|  |  |  |  |  |  | when developed caused severe runoff, which since has stabilized. No info. on |
|  |  |  |  |  |  | whether there is an issue with pesticides in runoff from greens, etc. |  |
| Carp. 6 | Little Mtn Rd | P29695 | Creek south of Eaglemont | Crk. BFW 6', BFD 4" - 12", large gravel/small cobble bed, no erosion, good cover |
| Carp. 7 | Little Mtn Rd | P29707 | Lang's beaver ponds |  | Extensive series of beaver ponds - owner says they plan to keep them intact |
| Carp. 8 |  | P29707 | 12" CMP forest road-crossing culv. | Partially squashed culvert, completed buried at U.s. end. Channel armored |
|  |  |  |  |  |  | owner says creek floods here once each year. Channel D.S. 6' wide with 4' high |
|  |  |  |  |  |  | incised banks, eroded, concrete debris armoring |  |  |
| Carp. 9 | Little Mtn Rd | P29707 | Pond and dam overflow | Part of creek is diverted into Lang's largest pond. Earth dam in questionable |
|  |  |  |  |  |  | condition. Pond overflow is a 3' rcc culvert. Crown is about 3' below top of |
|  |  |  |  |  |  | dam, invert perched 4', channel scoured DS. Headgate (weir) elev. at inlet |
|  |  |  |  |  |  | is about at top of culvert. L.O. says overflow at high Q is eroding the dam. |
| Carp. 10 | Little Mtn Rd | P29707 | 24' x 12' driveway bridge | Lang's driveway, 12" concrete slab bridge. Not constricting crk. Skunk cabbage, |
|  |  |  |  |  |  | good vegetation cover, but only 15' from LM Road. |  |  |
| Carp. 11 | Little Mtn Rd | P29707 | 18" rcc road crossing culvert | Small scour hole at outlet. Undersized - probably backs up water at Lang's |
|  |  |  |  |  |  | driveway - wetland conditions (skunk cabbage) on F/P upstream. DS is forested. |
| Carp. 12 | Little Mtn Rd | P29707 | Dug pond and gravel pit | Pond, with horse arena and gravel pit upslope, not buffers, etc. Appears to be |
|  |  |  |  |  |  | isolated from Carpenter Creek (no outlet culvert found) |  |  |
| Carp. 13 | Little Mtn Rd | P29719 | __" driveway crossing culvert | (hasn't been field checked) |  |  |  |  |
| Carp. 14 | Little Mtn Rd | P29715 | 52' x 9' railcar bridge and weirs | Lee property. Farm road over RR car bridge. Two log grade control weirs below |
|  |  |  |  |  |  | bridge for 2'-deep pools DS, gravel bar US. Salmon fry seen 7/15/04. Channel |
|  |  |  |  |  |  | D.S.BFW 11', BFD 18", gravel bottom, minor bank erosion. Backwatered by |
|  |  |  |  |  |  | beaver dam (Carp. 24) |  |  |  |  |  |
| Carp. 15 | Little Mtn Rd | P29715 | Pastures and PEME wetland | Horse pastures either side of creek fenced by minimal buffer. Pasture north of |
|  |  |  |  |  |  | creek is very muddy and or flooded, even in July, backwatered by beaver dam. |
| Carp. 16 | Little Mtn Rd | P29715 | Confluence of west trib. | Trib from east side of Little Mtn runs through flooded pasture. 5' wide x 3' deep. |
| Carp. 17 | Little Mtn Rd | P29653 | Large headwater PFOW wetland | Big intact PFOW wetland forms headwater of west trib. Partially isolated by road |
| Carp. 18 | Little Mtn Rd | P29653 | 18" rcc road crossing culvert | Drains wetland under Little Mountain Road. |  |  |  |
| Carp. 19 | Little Mtn Rd | P29715 | Beaver Dam |  | Perennial beaver dam backwaters creek & floods pasture. L.O. has tried to |
|  |  |  |  |  |  | remove it in the past but it gets re-built. Creek DS of dam BFW 12', BFD 8", |
|  |  |  |  |  |  | sand/gravel bed. Mostly dry 7/15/04, but has some freshwater mussels in it. |
|  |  |  |  |  |  | Large salmonberry PSS and alder wetland on F/P downstream. |  |
| Carp. 20 | Little Mtn Rd | P29715 | Horse access to creek |  | South end of pasture, unfenced stock access - trampled/eroded bank. Gravel bed |
| Carp. 21 | Little Mtn Rd | P29715 | Forested reach |  | Typical forested reach. BFW 16', BFD 18", some erosion at cut banks -max. 30' |
|  |  | P29727 |  |  |  | high. Lots of gravel bars, pools, LWD, and salmonid fy. Good riparian cover |
| Carp. 22 | Little Mtn Rd | P29731 | 34' x 14' railcar bridge |  | Channel at bridge BFW about 12', banks armored with riprap. |  |
| Carp. 23 | Little Mtn Rd | P29678 | Typical reach conditions | Mount Vernon forestland. Typ. BFW 11', BFD 2', F/P > 100' wide. Cut banks 30" |
|  |  |  |  |  |  | to 4' max. Several pools up to 30" deep, many salmonid fry. Also heron, frogs, |
|  |  |  |  |  |  | deer. Several old tires in creek. Bank soils are silty loam with clay lenses in |
|  |  |  |  |  |  | places. Buried LWD preserves channel structure. |  |  |
| Carp. 24 | E. Hickox Rd | P29678 | Typical reach conditions | Valley / channel slope increases in vicinity of MV ropes course. Typ. BFW 13', |
|  |  |  |  |  |  | BFD 15", F/P 40' (narrower). Large cobble bed, no bank erosion. Further down- |
|  |  |  |  |  |  | stream valley narrows to BFW 10', BFD 18", F/P 30' with large cobble/small |
|  |  |  |  |  |  | boulder bed. Good riparian cover. Fewer fry but many caddis fly larvae. |
|  |  |  |  |  |  | One large eroded face on right bank meander, 20' high. Erosion not too active. |
|  |  |  |  |  |  | Creek at archery range: BFW 14', BFD 18", FPW 75', cobble bed, nice riffles, |
|  |  |  |  |  |  | meanders, gravel bars, not eroded. Mature cottonwoods and alder on floodplain. |
| Carp. 25 | E Hickox Rd | P___ | 10' CMP road crossing culvert | New 98' long culvert at gravel pit access road. Slope good but needs more rock/ |
|  |  |  |  |  |  | gravel in bed. Constructed rock sill 10' DS from outlet drops 2.6' to bottom of |
|  |  |  |  |  |  | small pool IE 18" above pool use 7/22/04. Prob. a partial barrier, but plenty of fry |
|  |  |  |  |  |  | seen here and upstream 6/29 & 7/22. Leland Reese says culvert installed 1990 |
|  |  |  |  |  |  | after previous 3' diam. Culvert blew out in flood. Previous floods eroded banks, |
|  |  |  |  |  |  | including a now-stabilized cut left bank 50' DS. |  |  |
| Carp. 26 | Stackpole Rd | Various | right bank armoring and fill | Creek between E. Hickox and Cascade Ridge Rd. BFW 15' - 18' , BFD 12"- 18", |
|  |  |  |  |  |  | f/p 30-50'. Small (2' cut banks, small pools, debris jams. Along right bank some |
|  |  |  |  |  |  | armoring and concrete fill. Gravel road and camping area right to creek bank with |
|  |  |  |  |  |  | no buffer. At other places, decent 2nd growth forest buffer or ivy & blackberry |
|  |  |  |  |  |  | hedges. See field notes. |  |  |  |  |
| Carp. 27 | Stackpole Rd | P16253 | Left bank trib and fill |  | Small seasonal trib. Left bnk 12" wide x 4" deep. Dry in July. On right bank is |
|  |  |  |  |  |  | concrete fill and wood shed, ivy and blackberry (#20374 Stackpole Road) |
| Carp. 28 | Stackpole Rd | P16253 | Confl. Of Lake Ten Creek | Left bank about 150' u.s. of Casc. Ridge Road. BFW 3', BFD 18", small flow |
|  |  |  |  |  |  | 7/22/04. Decent forest cover. Sand accum. at mouth, no scour. |  |
| Carp. 29 | Casc. Ridge | P16253 | 7' CMP road crossing culvert | 42' long, some rock, gravel in bed but not enough. About 8' d.s. is a rock sill |
|  |  |  |  |  |  | stepping down to a pool (not a fish barrier). Knotweed along road shoulder. |
| Carp. 30 | Stackpole Rd | P16277 | Confluence with Stackpole Crk | About 50' DS of road crossing. Creek is a ditch, 6' wide x 4' deep clogged with |
|  |  |  |  |  |  | knotweed and canary grass. Carp. Crk DS is clogged with blackberry and |
|  |  |  |  |  |  | nightshade. |  |  |  |  |  |
| Carp. 31 | Stackpole Rd | P16275 | Water withdrawal |  | Small water intake pipe and pump at #20338 Stackpole Rd. |  |
| Carp. 32 | Stackpole Rd | P16297 | #20326 SP Rd Driveway bridge | 24' x 12' wood bridge. No buffer on left bank (road on right bank). Channel |
|  |  |  |  |  |  | clogged with nightshade (Densmore) |  |  |  |
| Carp. 33 | Stackpole Rd | P101006 | #20302 SP Rd driveway bridge | 24' x 16' concrete bridge. No buffer, channel clogged with vegetation (Urling) |
| Carp. 34 | Stackpole Rd | P16295 | # 20274 SP Rd. driveway bridge | 20'x 12' wood bridge. No buffer, channel clogged with veg. (Sanchez/Northey) |
| Carp. 35 | Stackpole Rd | P16301 | #20250 SP Rd driveway bridge | 16' x 16' concrete bridge, open pasture, no buffer (White) |  |  |
| Carp. 36 | Stackpole Rd | P16283 | #20196 SP Rd driveway bridge | 20' x 30' wide, falling apart (Roque) |  |  |  |
| Carp. 37 | Stackpole Rd | P16278 | #20156 SP Rd driveway bridge | 12' x 20'wood bridge. Trees on hillside reach to left bank s. of here. Blueberry |
|  |  |  |  |  |  | farm across road to west (Pearson) |  |  |  |
| Carp. 38 | Stackpole Rd | P16319 | #20134 SP Rd driveway bridge | New 12' x 20 steel "Janicki" bridge. Tree buffer on left bank, channel not as |
|  |  |  |  |  |  | clogged with vegetation (Faley) |  |  |  |  |
| Carp. 39 | Casc Rdg Ct. | P108102 etc | Detention wetland and NGPA | Constructed detention wetland and overflow to NGPA wetland, prob. seeps to CC |
| Carp. 40 | Kanako Ln | P16314 | Road crossing bridge |  | 50' x 30' wood girder bridge. Girders 5' high. Lots of salmonid fry seen below |
|  |  |  |  |  |  | bridge 7/22/04. BFW about 25'. Channel clogged with vegetation. Lots of water |
|  |  |  |  |  |  | seeping out of left bank from drainage from wetlands on hillside to east. |
| Carp. 41 | Kanako Ln | P16584 | Confluence of Sandy Creek | Sand accumulation, clogged with canary grass and blackberry. Start of Hill Ditch |

| Sub-basin Name: Johnson Creek |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Johnson 01 | Johnson Rd | P16580 | Natural falls/LWD |  | Natural fish passage blockages. Other? (Don?) |  |  |
|  |  | P16643 |  |  |  |  |  |  |  |  |  |  |
| Johnson 02 | Johnson Rd | P16643 | Natural channel |  | Just above aggrad. zone, BFW = 9', BFD 6", FPW about 25' |  |
| Johnson 03 | Johnson Rd | P16598 | Re-routed channel |  | 20001 Johnson Rd. Farm buildings and home built on F/P of creek.. Creek routed |
|  |  |  |  |  |  | along left edge of F/P. Canary grass grown up over PEME wetland pasture. |
|  |  |  |  |  |  | Probably a lot of subsurface seepage. |  |  |  |
| Johnson 04 | Johnson Rd | P16713 | Aggraded channel |  | Severely aggraded channel about 2' higher in elevation than surrounding F/P; |
|  |  |  |  |  |  | frequently overtops berm and floods road. BFW 20', BFD 8", sand and small cobble. |
|  |  |  |  |  |  | cobble. Flow mostly subsurface in summer. |  |  |  |
| Johnson 05 | Johnson Rd | P16713 | 6' CMP road crossing culvert | About 40' long. Inlet filled (40" depth) with sand / gravel. Outlet dredged Fall '04 |
|  |  |  |  |  |  | U.S. of culvert, creek BFW 8', BFD 30" - constrained between road and hillside |
| Johnson 06 | Johnson Rd | P16713? | Confluence with Hill Ditch | Flat grade, sediment delta dredged out Fall '04. Continuing problem area for |
|  |  |  |  |  |  | flooding. |  |  |  |  |  |  |
| Sub-basin Name: Sandy Creek |  |  |  |  |  |  |  |  |  |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Sandy 01 | Kanako Ln | P16584 | 4' CMP road crossing culvert | Gravel bed, not blocking |  |  |  |  |
| Sandy 02 | Kanako Ln | P16584 | No buffer along road |  | Sandy Creek diverted north along K Lane. BFW 6', BFD 18". Gravel/cobble |
|  |  |  |  |  |  | bed. Right bank armored, within 10' of road. Road about 3' higher than creek |
|  |  |  |  |  |  | bed. Blackberry hedge along left bank, some erosion along left bank. |  |
| Sandy 03 | Kanako Ln | P16584 | 42" CMP driveway culvert | 22' long culvert to #19046 Kanako Lane. Not a fish passage barrier |  |
| Sandy 04 | Kanako Ln | P16584 | Confluence with Hill Ditch | Confluence area has accumulated sediment and clogged with canary grass. |

| Sub-basin Name: Bulson Creek - South Fork |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Bulson SF 01 | Bulson Rd | P17684 | headwaters |  | Upstream creek originates in pasture wetland area |  |  |
| Bulson SF 02 | Bulson Rd | P17421 | Farm Pond |  | (Field check). |  |  |  |  |  |
| Bulson SF 03 | Bulson Rd | P17422 | 1' rcc road crossing culvert | Undersized. PSS wetland on F/P U.S.(water backed up). Houses on uplands |
| Bulson SF 04 | Bulson Rd | P17391 - | Alpaca pasture with no buffer | Hobby farms; alpaca grazing in PEME wetland, creek partially fenced |  |
|  |  | P17393 |  |  |  | but no buffer either sides. Expensive large houses on uplands. |  |
| Bulson SF 05 | English Rd | P17141 | 36" rcc road crossing culvert | Undersized culvert under a large road fill. Inlet partially blocked with gravel. U.S. |
|  |  |  |  |  |  | channel BFW about 7', BFD 8" FPW 20' gravel bed. OK forest on slopes of ravine |
|  |  | P118058 |  |  |  | Outlet nearly completely blocked with gravel and branches. Impassible to fish. |
|  |  |  |  |  |  | Observed salmonid fry in pool D.S. of culvert 10-29-04 |  |  |
| Bulson SF 06 | English Rd | P117119 | Confluence with Middle Fork | (no site visit) |  |  |  |  |  |
| Bulson SF 07 | SR 534 | P99255 | 6' steel road crossing culvert | New, with 6" gravel in bed. Not blocking. Adequate forest buffer upstream |
| Bulson SF 08 | SR 534 | P16679 | Concrete fishway |  | County installed concrete pool and weir fishway at culvert outlet in 2000(?) |
|  |  |  |  |  |  | Channel d.s. of fishway gravel & cobble bed, BFW 14', BFD 12", F/P >100' |
|  |  |  |  |  |  | Intact cedar and salmonberry forest |  |  |  |
| Bulson SF 09 | Okerlund Dr. | P16685 | Confluence of N, S Frks | Forested area designated as PCA. (No site visit) |  |  |
| Sub-basin Name: Bulson Creek - Middle Fork |  |  |  |  |  |  |  |  |  |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Bulson MF 01 | SR 534 | P17162 | Gravel quarry |  | Wilder Construction Co. quarry. Seasonal drainages eventually flow to PFOW |
|  |  |  |  |  |  | wetlands and then crk. No major runoff problems noted April '04 site visit. |
| Bulson MF 02 | SR 534 | several | highway runoff |  | SR 534 runs along the creek, minimal or no buffer along shoulder in places. |
|  |  |  |  |  |  | Creek floodplain is primarily PSS or PFOW wetland. |  |  |
| Bulson MF 03 | English Rd | P17098 | Road crossing culverts | Four culverts: 36" CMP, 30" rc, plus 24" CMP overlfow and 24" rc overflow. All |
|  |  |  |  |  |  | are partially blocked with sediment, evidence of flooding. |  |  |
| Sub-basin Name: Bulson Creek - Main (North) Fork |  |  |  |  |  |  |  |  |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Bulson NF 01 | Estate Drive | P105737 | 42" CMP road crossing culvert | Not perched. OK buffer. Note u.s. creek location on tax map is incorrect |
|  |  |  |  |  |  | Rock-lined road swales drain to Lake 16 and creek |  |  |
| Bulson NF 02 | Lake 16 Lane | P83818 | ___ Road crossing culvert | Forested floodplain, channel in good shape |  |  |  |
| Bulson NF 03 | Lake 16 Rd | P17147 | Reference condition? |  | U.S. of road, crk runs through little valley of mature fir and cedar. Bed is either |
|  |  |  |  |  |  | gravel or on ledge, meandering, pools, LWD. FPW 25', BFW 20', BFD 12" typical |
| Bulson NF 04 | Lake 16 Rd | P17158 | 3 x 36" CMP road culverts | Culverts about 36' long, outlets perched about 18" above small scour pool |
| Bulson NF 05 | Lake 16 Rd | P16640 | Houses - creek modifications | About 300' of channel D.S. of road with several modifications. One roof drain, |
|  |  |  |  |  |  | 2, 2" PE water intake pipes, two sections of R. bank armored with timber and |
|  |  |  |  |  |  | concrete blocks, a small concrete block dam. No obvious septic seepage noted |
| Bulson NF 06 | Hermway Hgts | P16689 | Waterfall - fish pass. blockage | Behind house #20810 HH Rd, an approx. 60' high water fallover natural ledge |
|  |  |  |  |  |  | Some dumping or yard waste and eroded banks U.S. (in a steep wooded ravine) |
| Bulson NF 07 | Okerlund Dr | P16685 | Confluence of N, S Frks | Forested area designated as PCA. (No site visit) |  |  |
| Bulson NF 08 | Bulson Rd | P16683 | Driveway bridge |  | Driveway to #20825 Bulson Rd. 30'(?) bridge. U.S. channel BFW 10', BFD 18" |
|  |  |  |  |  |  | 50' F/P. Left F/P rcg, right F/P forested. Channel partially clogged with rcg |
| Bulson NF 09 | Bulson Road | P16674 | Canary grass floodplain | D.S. of driveway bridge, wetland floodplain grown over with rcg and blackberry. |
| Bulson NF 10 | Bulson Road | P16740 | 2 X 36" RCC road culverts | About 30' long, floods frequently (undersized). Low road profile. Cty gauging stn. |
| Bulson NF 11 | Bulson Road | P16740 | Dredged channel |  | D.S. of road, BFW 8', BFD 12", FP about 80' - PEME wetland, gravel channel, |
|  |  |  |  |  |  | dredge spoils on right bank - gravel aggradation. |  |  |
| Bulson NF 12 | Bulson Road | P16739 | Boon Dairy |  | SCD WQ monitoring here. No buffer on channel. Dairy barns on upland terrace. |
| Bulson NF 13 | Bulson Road | P16739 | Confluence with Hill Ditch | Farm bridge and manure line crossing of Hill Ditch. No buffer. |  |

| Sub-basin Name: Starbird Creek |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Starbird 01 | Tyee Rd | P17364 | 18" CPP culvert, farm pond | Culvert under Tyee Road; unmapped trib to Starbird Creek |  |
| Starbird 02 | Tyee Rd | P17361 | PEME wetland |  | North of Tyee Road, all reed canary grass |  |  |  |
| Starbird 03 | Tyee Rd | P17386 | PFOW wetland |  | Large wetland both sides of road - cedar, alder, salmonberry, frogs |  |
| Starbird 04 | Tyee Rd | P17386 | 24" RCC culvert |  |  |  |  |  |  |  |  |
| Starbird 05 | Tyee Rd | P17386 | Old RR grade |  | Pilchuck Tree Farm access road along old English RR grade, creek probably |
|  |  |  |  |  |  | relocated along quarter section line east of rr grade |  |  |
| Starbird 06 | Starbird Rd | P17386 | PEME wetland |  | PFOW opens up into an abandoned pasture/canary grass wetland downstream, |
|  |  |  |  |  |  | Potential CREP buffer site |  |  |  |  |
| Starbird 07 | Starbird Rd | P113102 | Road culverts |  | 24" RCC, 24" CMP; PSS wetland north of road |  |  |  |
|  |  | P17767 |  |  |  | Creek through pasture - no buffer for about 200 feet, then enters forest |
| Starbird 08 | Starbird Rd | P17764 | 24” culvert |  |  | Deeply buried culvert at sharp corner/intersection with Odessa Road. |
|  |  |  |  |  |  | Outlet perched 1' with small plunge pool. Probable fish passage barrier |
| Starbird 09 | Starbird Rd | P17764 | Forested ravine |  | Small, steep ravine with good alder and cedar cover, gravel bed |  |
| Starbird 10 | Starbird Rd | P17837 | 18" rcc culvert |  | Undersized culvert under SB road. Rock armoring at outlet blocks passage, |
|  |  |  |  |  |  | but logged over ravine upstream is too steep for habitat. |  |  |
| Starbird 11 | Starbird Rd | P17836? | Driveway along creek |  | #21730 SB Rd. New gravel driveway alongside/within 10' of creek. Needs a buffer |
| Starbird 12 | English Grade | ? (Sno Cty) | 24" rcc culvert |  | At county line. Culvert outlet buried 18" with gravel. Upstream drains from a |
|  |  |  |  |  |  | PEME pasture wetland. L.O. planted firs on upland slopes of pasture |  |
|  |  |  |  |  |  | Small ravine downstream, good riparian forest. BFW 5', BFD 8", gravel bed. |
| Starbird 13 | Starbrook Lane | P17833 | 36" CMP road culvert |  | Culvert not perched, good riparian buffer. Creek downstream is mis-mapped |
|  |  |  |  |  |  | on tax parcel sheet. Seems to flow into a large forested wetland east of Fremali |
|  |  |  |  |  |  | Lane and then ends. Does not cross Fremali Ln and is not a trib. of Starbird Cr. |
| Starbird 14 | Fremali Lane | P17789 | 5' cmp culvert |  | BFW of creek near crossing about 12', BFD about 3'. Narrow buffer of alder and |
|  |  | P17794 |  |  |  | spirea. Horse, sheep pastured on 2 lots ds of crossing - could use wider buffers. |
| Starbird 15 | Fremali Lane | P17800 | 12" CMP culvert |  | Drains small seasonal swale under Fremali Lane |  |  |
| Starbird 16 | Starbird Crk Ln | P17786 | 24" CMP culvert (left) |  | Left culvert perched 1 foot, right culvert perched 2' - should determine if this is a |
|  |  |  | 30" CMP culvert (right) |  | fish passage barrier. |  |  |  |  |  |
| Starbird 17 | Bulson Road | P83085 | 8' RC culvert |  | Culvert OK, channel in good shape - gravel bars, etc.. Big cedars, etc. on F/P |
| Starbird 18 | Bulson Road | P83085 | Pond outlet |  | (Haven't visited the site yet) |  |  |  |  |
| Starbird 19 | Bulson Road | P83086 | confluence with Fisher Crk | (Haven't visited the site yet) |  |  |  |  |

| Sub-basin Name: Fisher Creek |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Road | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Fisher 01 | 24th Ave. NW |  | 2' CMP culvert crossing | Small unmapped trib through logged over area growing back up in blackberry, etc |
| Fisher 02 | English Grade Rd |  | 2' CMP culvert crossing | Unmapped trib. Downstream of EG Rd BFW 2', BFD 6" in mature cedar forest |
| Fisher 03 | 24th Ave. NW |  | 2' RCC culvert crossing | Southernmost trib of Fisher. Little ravine with natural ledge creek bed. Culvert |
|  |  |  |  |  |  | outlet perched (above ledge) about 1 foot - probably blocking. Mature cedars. |
| Fisher 04 | English Grade Rd |  | 18" RCC crossing |  | This trib. US of road blackberry thicket. DS of road culvert outlet broken, perched |
|  |  |  |  |  |  | about 1 ft. Minimal alder buffer in pasture, cattle grazing near creek. No fencing? |
| Fisher 05 | English Grade Rd |  | Trestle Bridge |  | Middle upper fork crossing in well forested ravine. Channel in good shape, gravel |
|  |  |  |  |  |  | gravel and cobble bed, meandering channel, mature trees on F/P |  |
| Fisher 06 | 324th ST. NW |  | Farm pond |  | Small dug pond on left bank. Seems to be filled by creek - either pumped or |
|  |  |  |  |  |  | diverted, but does not block creek |  |  |  |  |
| Fisher 07 | 324th St. NW |  | 4' CMP culvert crossing | Creek banks at inlet actively eroding, culvert partially filled with gravel. Bank |
|  |  |  |  |  |  | stabilization? How is this affected by the dug pond? |  |  |
| Fisher 08 | 324th St. NW |  | Confluence of N & S tribs | In forest - haven't visited yet |  |  |  |  |
| Fisher 09 | Brandstrom Rd |  | Roadside ditch |  | Creek runs about 100' north along road in an eroding ditch - sediment source |
| Fisher 10 | Brandstrom Rd |  | 4' CMP culvert crossing | DS of road, creeks run through pasture with minimal alder and spirea buffer. |
|  |  |  |  |  |  | A lot of reed canary grass in channel. Potential CREP site |  |  |
| Fisher 11 | 324th St. NW |  | 2' CMP culvert crossing | Moderately incised channel in pasture. Essentially no buffer. Near pipeline route |
| Fisher 12 | 44th Ave. NW |  | Gas pipeline route |  | Creek runs through open pasture with no riparian buffer. Check location of |
|  |  |  |  |  |  | pipeline ROW and their requirements related to planting a buffer. |  |
| Fisher 13 | Bulson Road | P17746 | 5' CMP culvert with |  | Main (lower) culvert partially filled with sediment. Upper (overflow) culverts |
|  |  |  | 2 30" CMP overflows |  | outlet direct to pasture |  |  |  |  |
| Fisher 14 | West Bulson Rd | P17746 | Seasonal swale |  | Swale through a cow pasture connects to road ditch, then to Fisher Creek |
| Fisher 15 | Bulson Road | P17746 | Unfenced cattle access | Riparian area nearest the culvert outlets is not fenced, allowing cattle access |
|  |  | P17744 | No buffer along creek |  | Cow pasture with no buffer. Fenceline at creek bank minimally excludes cattle. |
| Fisher 16 | Bulson Road | P17730 | 20' x 10' driveway bridge | AT # 23502 Bulson Road. Wood bridge, channel ok. Lawn on RB F/P floods. |
| Fisher 17 | Bulson Road | P83086 | Confluence with Starbird | (Same as ID No. Starbird 19. Haven't visited site yet) |  |  |
| Fisher 18 | Starbird Road | P17692 | Incomplete buffer |  | A few cedars in pasture on right bank, but RB buffer should be improved (LB ok) |
| Fisher 19 | Starbird Road | P17689 | 4' rcc culvert under SB Rd |  |  |  |  |  |  |  |
| Fisher 20 | Starbird Road | P17689 | Fishway, incomplete buffer | County log weir fishway. L.o.'s minimal tree buffer should be improved. |
| Fisher 21 | Starbird Road | P17696 | Seasonal trib through PEME | Unmapped seasonal trib under SB road and through open pasture wetlands |
| Fisher 22 | Starbird Road ? | P17690 | RR flat car bridge |  | Bridge over Fisher Creek - unpaved forest road, probably to access pipeline |
| Fisher 23 | Starbird Road ? | P17425 | Gas pipeline crossing |  |  |  |  |  |  |  |  |
| Fisher 24 | Bulson Road ? | P17425 ? | Eroding bank |  | Actively eroding right bank at sharp meander. |  |  |  |
| Fisher 25 | Starbird Road | P17413 | Creek confluence |  | Confluence with unmapped seasonal trib (left bank) |  |  |
| Fisher 26 | Bulson Road ? | P17413 |  |  |  | Relatively pristine reach of creek. Mature 2nd growth forest, bed is cobble and |
|  |  |  |  |  |  | small boulder with LWD, pools, gravel bars, etc. BFW 10'-15', 25'-30' in places, |
|  |  |  |  |  |  | BFD 2' - 3'. F/P width around 50; (ravine) |  |  |  |
| Fisher 27 | Bulson Road | P17407 | Clear cut to right bank |  | Large clear cut on right bank with minimal if any buffer. Did DNR permit this? |
| Fisher 28 | North Starbird Rd | P116185 | Eroding left bank |  | Left slopes of ravine have several steep slumps/blow outs. Area designated as |
|  |  | et al. |  |  |  | NGPA - important to enforce 200' set backs. |  |  |  |
| Fisher 29 | North Starbird Rd | P17478 | Road culverts |  | 18" CPP culvert drains pasture swale across Bella Vista Ln. to 36" CMP under N. |
|  |  |  |  |  |  | St. Rd. Joins road ditch under 18" CPP to form trib. |  |  |
| Fisher 30 | North Starbird Rd. | P119001 | Riparian buffer |  | At parcel S end a few cedars on RB, blackberries on LB. Good buffer at N. end |
| Fisher 31 | Cedardale Rd | P119001 | Trib confluence |  | Confluence of trib from North Starbird Road development. BFW 5', BFD 18" |
|  |  |  |  |  |  | large cobble bed (must get a lot of scour at times) |  |  |
| Fisher 32 | Cedardale Rd | P119001 | Iron sulfide seep |  | Left bank seep of orange filament algae with septic smell |  |  |
| Fisher 33 | Cedardale Rd | P17462 | 8'x8' rcc box culvert |  | Creek U.S.: cobble, BFW 30', BFD 3', F/P about 50' wide, slightly incised, |
|  |  |  |  |  |  | forest cover |  |  |  |  |  |
| Fisher 34 | Cedardale Rd | I-5 ROW | Fishway |  |  | Concrete pool and chute fishway constructed by WDFW |  |  |
| Fisher 35 | I-5 | I-5 ROW | culverts? |  |  | Culverts under I-5 (check) |  |  |  |  |
| Fisher 36 | Franklin Rd | P17459 | Junkyard, minimal buffer | Right bank has minimal buffer between junk yard. Channel looks OK |  |
| Fisher 37 | Franklin Rd | P17467 | Box culvert |  |  | RCC box culvert, size? Not blocking. Creek downstream in good shape with |
|  |  |  |  |  |  | gravel/cobble bed and mature tree buffer. |  |  |  |
| Fisher 38 | Franklin Rd | P17518 | Confluence with Little Fisher | POFW - alder, salmon berry wide floodplain. Just below confluence, left bank |
|  |  |  |  |  |  | is a riprap-armored dike. A few rootwads installed on l bank for habitat features |
| Fisher 39 | DD3 dike | P175189 | Confluence with Hill Ditch |  |  |  |  |  |  |  |

| Sub-basin Name: Little Fisher Creek - East Fork |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| LF E Frk 01 | W. Bulson Rd | P17739 | Farm ponds, wetlands | Headwaters of east trib of E. Fork LF Crk. PSS/PFOW wetlands, two farm ponds |
| LF E Frk 02 | Starbird Rd | P17703 | Pasture, no buffer |  | PEME wetlands in pasture with no buffer, creek ditched before flowing under I-5 |
| LF E Frk 03 | I-5 | I-5 ROW | 4' CMP culvert |  | Very long (>300') run under I-5 through culvert. Unknown if a velocity barrier. |
| LF E Frk 04 | Pacific Hwy S. | I-5 ROW | Confluence with E. Fork | Confl. with E. Fork. BFW below confl. 6', BFD 2' gravel bottom, Headcut (Item# 12) |
| LF E Frk 05 | 324th St. NW |  | Culvert and wetland |  | 2' ? Culvert under road, inlet & outlet buried. Extensive cedar, spirea, salmon- |
|  |  |  |  |  |  | berry wetland along floodplain both sides (culvert undersized?) |  |
| LF E Frk 06 | County Line Rd | P90029 | Wetlands |  |  | D.S. of road, extensive PSS wetland and forested floodplain. U.S.of road, creek |
|  |  | (Sno Cty) |  |  |  | ditched along driveway fill. Mostly PFOW except where filled by houselots. A few |
|  |  |  |  |  |  | cows grazing on yards, creek fenced |  |  |  |
| LF E Frk 07 | County Line Rd | P90029 | Road crossing culverts | 2 x 24" rcc culverts |  |  |  |  |  |
| LF E Frk 08 | Bruun Rd | P17661 |  |  |  | Old pasture grown up as rcg PEME with narrow spirea/willow buffer. |  |
|  |  | P17666 |  |  |  | BFW about 4', BFD 8", sandy bottom. Resident (B. Quist) says no fish ever seen |
|  |  |  |  |  |  | in the creek in that area. |  |  |  |  |
| LF E Frk 09 | Bruun Rd | P17667 | 2' CMP culvert road crossing | About 30' long, outlet percehd 6". D.S. creek along back yard with no buffer |
| LF E Frk 10 | Bruun Rd | P17660 | 3' CMP driveway culvert | About 20' long, not blocking. Creek channel clogged with rcg and willow. |
| LF E Frk 11 | Pacific Hwy S. | P17616 | 4' CMP road culvert |  | About 150' long under Pac Hwy S. No buffer d.s., blackberry thicket u.s. |
| LF E Frk 12 | Pacific Hwy S. | I-5 ROW | Head cut |  |  | Small (about 12") headcut u.s. of confluence with E. trib. Scour area? |  |
| LF E Frk 13 | Milltown Rd | I-5 ROW | 5' CMP culvert road crossing | About 150' long under Milltown Rd. Narrow tree buffer l. bank, I-5 shoulder |
|  |  |  |  |  |  | along R bank. Probably a velocity barrier |  |  |  |
| LF E Frk 14 | Bonnie View Rd | P17584 | 5' CMP culvert road crossing | Over 150' long, massive road fill in natural forested ravine. Prob. velocity barrier |
|  |  | P17603 |  |  |  | Crude rock weir structure at inlet. Needs weirs or baffles in culvert at least |
| LF E Frk 15 | Clarence Rd | P17622 | 8' CMP culvert road crossing | Concrete wingwalls at inlet, gravel in bed. U.S. forested (cedar) buffer in good |
|  |  |  |  |  |  | shade. D.S. one lawn on right bank with no buffer, but otherwise ok |  |
| LF E Frk 16 | Franklin Rd | P17475 | Natural fish passage barrier | LWD in creek bed forms about a 3' fall, good gravel bed accum. U.S. Forested |
| LF E Frk 17 | Franklin Rd | P17469 | 4' RCC culvert road crossing | Outlet perched 2', somewhat blocking |  |  |  |
| LF E Frk 18 | Franklin Rd | P17469 | Channel above confluence | BFW about 15', nice gravel bed, Decent tree buffer for 100', then opens into fields |
| LFF E Frk 19 | Franklin Rd | P17469 | Confluence with West Fork | Open pasture in small valley. No buffer or fencing. Cattle trample and poop |
|  |  |  |  |  |  | in creek. Lots of juncus. Good gravel bed. Excellent site for CREP. |  |

| Sub-basin Name: Little Fisher Creek - West Fork |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| LF W Frk 01 | 324th St. NW |  | 6' CMP culvert road crossing | Creek channel about 8' BFW, low gradient, mucky. Extensive PFOW F/P wetland |
| LF W Frk 02 | County Line Rd |  | Farm pond and dam |  | Old concrete dam impounds creek - complete fish passage barrier. Steel grating |
|  |  |  |  |  |  | bridge over creek d.s. of dam (O'Malley property) |  |  |
| LF W Frk 03 | County Line Rd | P17585 | 4' CMP road crossing culvert | Thick forest and blackberry hedge upstream - no access to creek |  |
| LF W Frk 04 | Milltown Rd | P17633 | 4' rcc box culvert road crossing | Extensive rock gabion wall fill across valley has formed large PFOW and PSS |
|  |  |  |  |  |  | wetlands upstream. 4' culvert outlets to a fishway (#05) |  |  |
| LF W Frk 05 | Milltown Rd | P17629 | Concrete fishway |  | Old WDFW (?) pool and weir fishway raises creek to level of box culvert. Creek |
|  |  |  |  |  |  | d.s. goes 100' through lawns (no buffer) then into small forested valley |
| LF W Frk 06 | Franklin Road | P17469 | Confluence with E. Fork | Open pasture in small valley. No buffer. See # E Frk 19. Many coho fry seen 6/05 |
| LF W Frk 07 | Franklin Road | P17468 | 5' rcc box culvert |  | Driveway crossing to # 22716 Franklin Road. Gravel in culvert, not blocking. |
|  |  |  |  |  |  | U.S. creek flows through pasture (PEME wetland?) with no buffer or cattle fencing. |
| LF W Frk 08 | Franklin Road | P17466 | Dike, ditching |  | D.S.of #22716 driveway, creek runs along dike. Channel is partially ditched but |
|  |  |  |  |  |  | has some areas of natural gravel bottom. No buffer or cattle fencing at all. RCG |
|  |  |  |  |  |  | clogs channel in some places. |  |  |  |  |
| LF W Frk 09 | Franklin Rd | P17518 | Confluence with Fisher Crk | (See Item # Fisher 38). |  |  |  |  |

| Sub-basin Name: Hill Ditch |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ID No. | Nearest Rd. | Parcel No. |  | Feature |  |  |  |  | Comment |  |  |  |
| Hill Ditch 01 | Kanako Lane | P16584 | Confluence with Sandy Creek | Carpenter Creek becomes hill ditch here. Sediment deposition zone requires |
|  |  |  |  |  |  | dredging. Channel clogged with rcg. No buffer |  |  |
| Hill Ditch 02 | Stackpole Rd | P16585 | Cattle pasture, no buffer | Benson property. |  |  |  |  |  |
| Hill Ditch 03 | Stackpole Rd | P16590 - | Shrub wetland |  | Extensive PSS open water wetland behind left bank spoil mounds. A few trees |
|  |  | P16576 |  |  |  | but generally no buffer. |  |  |  |  |
| Hill Ditch 04 | Johnson Rd | P16598 | Forest road crossing shown on map but not verified |  |  |  |  |  |
| Hill Ditch 05 | Johnson Rd | P16713(?) | Confluence with Johnson Crk | Frequent sediment deposition/ flooding area. No buffer |  |  |
| Hill Ditch 06 | Johnson Rd | P16713(?) | Johnson Road bridge |  | Concrete bridge. Span about 50' x 25' |  |  |  |
| Hill Ditch 07 | Johnson Rd | Various | Reach with no buffer |  | U.S. of Boon Farm. Fallow field west of 30' DD ROW |  |  |
| Hill Ditch 08 | Bulson Road | P16739 | Manure pipeline crossing | Boon Farm. Also a farm vehicle bridge here |  |  |  |
| Hill Ditch 09 | Bulson Road | P16739 | Confluence with Bulson Crk |  |  |  |  |  |  |  |
| Hill Ditch 10 | SR 534 | P16746 | CREP buffer |  | Anderson |  |  |  |  |  |  |
| Hill Ditch 11 | SR 534 | P16990 | Hwy crossing bridge |  | 80' x 28' concrete bridge on SR 534 |  |  |  |
| Hill Ditch 12 | SR 534 | P16990 | Reach with no buffer |  |  |  |  |  |  |  |  |
| Hill Ditch 13 | Conway Hill Rd | P16931 | Road crossing bridge |  | 50' x 16' concrete bridge. Channel in ok shape, good left bank (hillside) buffer |
| Hill Ditch 14 | Conway Hill Rd | P16931 | Reach with no buffer |  | 30' DD ROW then ditch (drains to Big Ditch), then open fields. Good LF buffer |
| Hill Ditch 15 | Cedardale Rd | P120629 | Bridge crossing |  | 80' x 30' concrete bridge |  |  |  |  |
| Hill Ditch 16 | Snowden Place | P17447 | Forested floodplain |  | Left bank floodplain forested, not protected by dike |  |  |
| Hill Ditch 17 | Cedardale Rd | P120629 | I-5 bridge crossings |  | Approx. 100' long bridges on both north and south lanes of I-5 |  |
| Hill Ditch 18 | Franklin Rd | P17450 | Reach with no buffer |  | Upper Fisher Slough at Dinghy Co. |  |  |  |
| Hill Ditch 19 | Franklin Rd | P17450 | Confluence with Fisher Crk. |  |  |  |  |  |  |  |
| Hill Ditch 20 | Several | Several | DD3 Dike |  |  | Along right bank from Kanako Ln to I-5. Incl. 30' easement on w. side. No buffer. |

Appendix 2: Soils

(Soil # 5-8) Barneston, (Soil # 49-50) Dystric Xerorthents- Barneston soils are on glacial outwash terraces and terrace escarpments.  The soils are very deep and somewhat excessively drained.  They formed in loess and volcanic ash underlain by glacial outwash.  The surface is covered with a mat of needles and twigs.  The surface layer and subsoil are gravelly loam, very gravelly sandy loam, or very cobbly sandy loam about 20 inches thick.  The substratum to a depth of 60 inches or more is very cobbly loamy sand, very gravelly loamy course sand, or extremely gravelly sand.  Dystric Xerorthents are on steep or extremely steep terrace escarpments.  The soils are very deep and excessively drained.  They formed in glacial outwash.  The surface is covered with a mat of needles, leaves, and twigs.  The surface layer is gravelly sandy loam about 4 inches thick.  The subsoil is gravelly loamy sand about 31 inches thick.  The substratum to a depth of 60 inches or more is stratified very gravelly sand and gravelly sand.  This unit is used as woodland and homesites.  If the unit is used for homesite development, the main limitations are steepness of slope and the risk of seepage from onsite sewage disposal systems.

(Soil # 16-20) Bow, (Soil # 35-38) Coveland- Bow soils are on glacial remnant terraces.  The soils are very deep and somewhat poorl           y drained.  They formed in glacial drift over glaciolacustrine sediment with a mantle of volcanic ash.  The surface is covered with a mat of leaves and twigs.  The surface layer and upper part of the subsoil are gravelly loam about 8 inches thick.  The lower part of the subsoil to a depth of 60 inches or more is clay loam over silty clay.  Coveland soils are on glaciated hills.  The soils are moderately deep and moderately well drained.  They formed in glacial till with an admixture of loess and volcanic ash.  The surface is covered with a mat of needles, leaves, and twigs.  The surface layer and upper part of the subsoil are gravelly loam about 20 inches thick.  The lower part of the subsoil and the substratum are very gravelly fine sandy loam over very gravelly sandy loam about 11 inches thick over dense glacial till.  Depth to dense glacial till ranges from 25 to 40 inches.  This unit is used as a woodland, hayland, pastureland, and homesites.  If the unit is used for homesite development, the main limitation is a perched seasonal high water table.

(Soil # 27-28) Chuckanut, (Soil # 22-24) Cathcart- Chuckanut soils are on hills and mountainsides.  The soils are deep and well drained.  They are formed in volcanic ash and colluvium derived from sandstone and needles, leaves, and twigs.  The surface layer and upper part of the subsoil are gravelly loam about 15 inches thick.  The lower part of the subsoil is gravelly sandy loam 14 inches thick over sandstone.  Depth to sandstone ranges from 40 to 60 inches. Cathcart soils are on glaciated plains, foothills, and mountainsides.  The soils are very deep and well drained.  They are formed in volcanic ash, glacial till, and sandstone.  The surface is covered with a mat of needles, leaves, and twigs.  The surface layer and subsoil are loam about 40 inches thick.  The substratum to a depth of 60 inches or more is gravelly sandy loam.  Most areas of this unit are used as woodland.  A few areas are used for homesite development; the main limitation is steepness of slope.  Soils of a minor extent in this soil unit are somewhat excessively drained (5-8) Barneston soils on terraces and moderately drained 146-149) Tokul soils on hills.

(Soil # 77) Jug- Jug soils are on terraces.  The soils are very deep and somewhat excessively drained.  They formed in volcanic ash and glacial outwash.  The surface is covered with at mat of needles, leaves, and twigs.  The surface layer is very gravelly loam about 7 inches thick.  The subsoil is extremely cobbly sandy loam over extremely cobbly loamy sand about 34 inches thick.  The substratum to a depth of 60 inches or more is extremely cobbly sand.  This unit is used as woodland.  The main limitations are steepness of slope and seasonal soil wetness.

(Soil # 80-81) Kindy- Kindy soils are on glacially modified mountainsides.  The soils are moderately deep and moderately well drained.  They formed in volcanic ash, loess, and glacial till.  The surface is covered with at mat of leaves, needles, and twigs.  The surface layer is gravelly silt loam about 4 inches thick.  The subsoil is very gravelly silt loam 15 inches thick.  The substratum is very gravelly loam 7 inches thick over dense glacial till.  Depth to dense glacial till ranges from 20 to 40 inches.  This unit is used as woodland and watershed.  The main limitations are steepness of slope, snowpack, and seasonal wetness.

(Soil # 146-149) Tokul, (Soil # 124-125) Skipopa- Tokul soils are on glacially modified hills.  The soils are moderately well drained.  They formed in volcanic ash and loess underlain by glacial till.  The surface is covered with a mat of needles, leaves, and twigs.  The surface layer and subsoil are gravelly loam about 34 inches thick.  The substratum is gravelly sandy loam about 5 inches thick over silica-cemented glacial till.  Depth to silica-cemented glacial till ranges from 20 to 40 inches.  Skipopa soils are on lakebed terraces.  The soils are very deep and somewhat poorly drained.  They formed in a mantle of loess and volcanic ash underlain by glaciolacustrine sediment.  The surface is covered with a mat of leaves and twigs.  The surface layer and subsoil are silt loam about 16 inches thick.  The substratum to a depth of 60 inches or more is silty clay.  This unit is used as woodland, pastureland, hayland, and homesites.  If this unit is used for homesite development, the main limitation is steepness of slope, a seasonal high water table, and very slow permeability.  Soils of a limited extent in this unit are poorly drained (10-11) Bellingham soils, and very poorly drained (97-98) Mukilteo soils in depressional areas, somewhat excessively drained (5-8) Barneston soils on terraces, (67-69) Hoogdal soils on terraces and terrace escarpments, (16-20) Bow soils on terraces and plains, (22-24) Cathcart soils on plains and foothills, (153-154) Vanzandt soils on plans and low mountainsides and (27-28) Chuckanut soils on hills.

(Soil #153-154) Vanzandt- Vanzandt soils are on glacially modified plains and low mountainsides.  The soils are moderately deep and moderately well drained.  They formed in volcanic ash and glacial till.  The surface is covered with a mat of needles, leaves, and twigs.  The surface layer and subsoil are very gravelly loam about 25 inches thick over dense glacial till.  Depth to dense glacial till ranges from 20 to 40 inches.  This unit is used as woodland.  The main limitations are steepness of slope and seasonal soil wetness.  Soils of a minor extent in this unit are somewhat excessively drained (5-8) Barneston soils on terraces and (49-50) Dystric Xerochrepts on escarpments and mountainsides.

Appendix 3: Well logs

| Sect. | Town. | Range | Well Logs to 25 Ft. Min. Depth | From | To | Bailer Test g/min | Ft. Drawdown | Hour | H2O Level Ft. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2 | 32 | 4E | Top Soil | 0 | 1 | 20 | 35 | 1 | 38 |
|  |  |  | Sandy Tan loam | 1 | 15 |  |  |  |  |
|  |  |  | Sandstone | 15 | 165 |  |  |  |  |
| 3 | 32 | 4E | Top Soil | 0 | 1 | 3 | 20 | 1 | 50 |
|  |  |  | Gravel/Brown Clay | 1 | 9 |  |  |  |  |
|  |  |  | Grey Clay Sand | 9 | 63 |  |  |  |  |
| 4 | 32 | 4E | Top Soil | 0 | 3 | 15 | 4 | 0.5 | 55 |
|  |  |  | Hard Pan | 3 | 62 |  |  |  |  |
| 5 | 32 | 4E | Top Soil | 1 | 2 | 10 | na | 1.5 | 128 |
|  |  |  | Dirt Gravel and Boulders | 2 | 14 |  |  |  |  |
|  |  |  | Hard Pan | 14 | 14 |  |  |  |  |
| 35 | 33 | 4E | Brown Clay | 0 | 8 |  |  |  |  |
|  |  |  | Brown Clay and Gravel | 8 | 15 |  |  |  |  |
|  |  |  | Grey Clay and Gravel | 15 | 58.5 |  |  |  |  |
| 34 | 33 | 4E | Top Soil | 0 | 2 | na | na | na | na |
|  |  |  | Brown Clay and Gravel | 2 | 10 |  |  |  |  |
|  |  |  | Grey Gravel and Clay | 10 | 22 |  |  |  |  |
|  |  |  | Grey Clay | 22 | 23 |  |  |  |  |
|  |  |  | Grey Gravel and Clay | 23 | 24 |  |  |  |  |
|  |  |  | Grey Clay | 24 | 27 |  |  |  |  |
| 33 | 33 | 4E | Top Soil | 0 | 2 | 10 | 1 | 1 | 215 |
|  |  |  | Brown Clay and Gravel | 2 | 24 |  |  |  |  |
|  |  |  | Grey Clay and Gravel | 24 | 125 |  |  |  |  |
| 32 | 33 | 4E | Hard Pan and Boulders | 1 | 30 | 20 | 8.5 | na | 60 |
| 31 | 33 | 4E | Dirty Sand and Gravel | 0 | 3 | 30 | 20 | na | 30 |
|  |  |  | Brown Clay | 3 | 20 |  |  |  |  |
|  |  |  | Blue Clay | 20 | 78 |  |  |  |  |
| 26 | 33 | 4E | Top Soil | 0 | 2 | na | na | na | na |
|  |  |  | Brown Sand Clay | 2 | 21 |  |  |  |  |
|  |  |  | Grey Clay and Gravel | 21 | 42 |  |  |  |  |
| 27 | 33 | 4E | Top Soil | 0 | 1 | 10 | 3 | 1 | 110 |
|  |  |  | Brown Sand Clay and Gravel | 1 | 12 |  |  |  |  |
|  |  |  | Grey Clay Course Gravel | 12 | 30 |  |  |  |  |
| 28 | 33 | 4E | Brown Gravel and Sand | 0 | 10 | Air test 30 gpm | na | na | 145 |
|  |  |  | Brown Sand | 10 | 16 |  |  |  |  |
|  |  |  | Grey Clay and Sand | 16 | 27 |  |  |  |  |
| 29 | 33 | 4E | Tan Clay | 0 | 16 | 2 | 140 | 2 | 50 |
|  |  |  | Grey Clay | 16 | 19 |  |  |  |  |
|  |  |  | Grey Clay and Fine Sand | 19 | 27 |  |  |  |  |
| 23 | 33 | 4E | Dirty Sand and Gravel | 0 | 10 | 15 | 60 | na | 1 |
|  |  |  | Blue Clay | 10 | 50 |  |  |  |  |
| 22 | 33 | 4E | Top Soil | 0 | 2 | 12 | 4 | 1 | 197 |
|  |  |  | Grey Hard Pan | 2 | 120 |  |  |  |  |
| 21 | 33 | 4E | Top Soil | 0 | 4 | 12 | na | 2 | 29.5 |
|  |  |  | Tan Clay and Water | 4 | 12 |  |  |  |  |
|  |  |  | Grey Clay | 12 | 18 |  |  |  |  |
|  |  |  | Grey Sandy Clay and Clam Shells | 18 | 27 |  |  |  |  |
| 20 | 33 | 4E | Top Soil | 0 | 3 | 10 | 0 | 1 | 128 |
|  |  |  | Hard Pan | 3 | 18 |  |  |  |  |
|  |  |  | Brown Clay | 18 | 57 |  |  |  |  |
| 13 | 33 | 4E | Sand | 0 | 33 | 15 | na | na | 5.6 |
| 16 | 33 | 4E | Brown Clay | 0 | 39 | 5 | 19 | na | 21 |
|  |  |  | Gravel Water | 39 | 45 |  |  |  |  |
| 17 | 33 | 4E | Top Soil and Gravel | 0 | 1 | Air test 30 gpm | 13 | na | 30 |
|  |  |  | Brown Clay | 1 | 19 |  |  |  |  |
|  |  |  | Blue Clay and Little Grave | 19 | 27 |  |  |  |  |
| 10 | 33 | 4E | Top Soil | 0 | 2 | Air test 1 gpm | 120 | 1 | 24 |
|  |  |  | Gravel and Silt | 2 | 11 |  |  |  |  |
|  |  |  | Bedrock | 11 | 124 |  |  |  |  |
| 9 | 33 | 4E | Topsoil | 0 | 1 | Air test 3.5 gpm | na | 1.5 | 79.5 |
|  |  |  | Brown Gravel Silt and Sand | 1 | 20 |  |  |  |  |
|  |  |  | Grey Gravel and Clay | 20 | 29 |  |  |  |  |
| 8 | 33 | 4E | Topsoil and Gravel | 0 | 1 | Air test 18 gpm | 58 | 1 | 8.5 |
|  |  |  | Brown Clay | 1 | 18 |  |  |  |  |
|  |  |  | Blue Silty Clay and Seashells | 18 | 22 |  |  |  |  |
|  |  |  | Water Silt and Seashells | 22 | 25 |  |  |  |  |
| 2 | 33 | 4E | Topsoil | 0 | 1 | Air test 15 gpm | na | 1 | 290 |
|  |  |  | Brown Clay | 1 | 12 |  |  |  |  |
|  |  |  | Grey Clay and Gravel | 12 | 32 |  |  |  |  |
| 3 | 33 | 4E | Fill | 0 | 5 | 75 | 190 | 1 | 375 |
|  |  |  | Brown Silt Sand and Gravel | 5 | 10 |  |  |  |  |
|  |  |  | Green Fractured Bedrock | 10 | 50 |  |  |  |  |
| 4 | 33 | 4E | Topsoil | 0 | 1 | 10 | 40 | 1 | 7 |
|  |  |  | Sand and Gravel | 1 | 12 |  |  |  |  |
|  |  |  | Brown Sandy Clay | 12 | 23 |  |  |  |  |
|  |  |  | Blue Clay | 23 | 37 |  |  |  |  |
| 35 | 34 | 4E | Topsoil | 1 | 3 | 10 | 320 | 1 | 60 |
|  |  |  | Blue Shale | 3 | 58 |  |  |  |  |
|  |  |  | Soft Shale and Dark Grey Clay | 58 | 130 |  |  |  |  |
| 34 | 34 | 4E | Topsoil | 0 | 1 | Air test 3 gmp | na | 1 | 40 |
|  |  |  | Brown Sand and Clay | 1 | 10 |  |  |  |  |
|  |  |  | Wet Sand | 10 | 12 |  |  |  |  |
|  |  |  | Grey Sandstone | 12 | 75 |  |  |  |  |
| 33 | 34 | 4E | Topsoil | 0 | 2 | 12 | 10 | 1 | 40 |
|  |  |  | Tan Hard Pan and Cobbles | 2 | 7 |  |  |  |  |
|  |  |  | Grey Hard Pan and Cobbles | 7 | 45 |  |  |  |  |
| 27 | 34 | 4E | Fill | 0 | 2 | na | na | na | none |
|  |  |  | Brown Gravel Sand | 2 | 10 |  |  |  | Well casing |
|  |  |  | Brown Clay and Gravel | 10 | 15 |  |  |  | broke at 380 ft. |

Appendix 4: Water Quality Monitoring Data

| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | 1 | BRFC | 9:35 | 12 | 62 | 6.68 | 2.6 |  | 50 |  |
|  | 2 | FRFC | 10:15 | 12 | 102 | 11.5 | 0.64 |  | 50 |  |
|  | 3 | 16BC | 11:25 | 14 | 89.2 | 8.94 | 0.59 |  | 50 |  |
|  | 4 | CEBC | 11:48 | 13 | 95.8 | 10.21 | 0.95 |  | 50 |  |
|  | 5 | DBCC | 12:05 | 13 | 64.2 | 6.74 | 0.77 |  | 30 |  |
|  | 6 | CNBR |  |  |  |  |  |  |  | no sample-culvert not active |
|  | 7 | UBCC | 12:20 | 14 | 58.7 | 5.78 | 0.93 |  | 50 |  |
|  | 18 | CHCC | 13:00 | 13 | 79 | 8.29 | 0 |  | 2 |  |
|  | 19 | UMJC | 13:15 | 12 | 98.1 | 10.5 | 1.03 |  | 50 |  |
|  | 10 | UMSC | 13:30 | 12 | 72.7 | 7.74 | 0.23 |  | 80 |  |
|  | 11 | UM10 |  |  |  |  |  |  |  | no sample-not active |
|  | 12 | GPCC | 13:50 | 13 | 124 | 13.22 | 2.33 |  |  |  |
| Winkler | FRFC | 11mg/L |  |  |  |  |  |  |  |  |
| FC | UMJC | 50 |  |  |  |  |  |  |  |  |
| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| 10/26/2004 | 1 | BRFC | 12:10 | 9.2 | 77.5 | 8.92 | 2.13 |  | 500 | been very dry--no rain |
|  | 2 | FRFC | 11:35 | 8.9 | 60.4 | 7.08 | 1.41 |  | 80 |  |
|  | 3 | 16BC | 12:30 | 11 | 53.8 | 5.97 | 1.86 |  | 4 |  |
|  | 4 | CEBC | 12:40 | 9.6 | 58.1 | 6.64 | 1.23 | N/A | 13 | GAUGE ABOVE WATERLINE |
|  | 5 | DBCC | 13:00 | 9.4 | 94.5 | 10.89 | 0.88 |  | 30 |  |
|  | 6 | CNBR | 12:50 | 9.8 | 74.2 | 8.1 | 4.41 |  |  |  |
|  | 7 | UBCC | 13:10 | 9.5 | 93.4 | 10.5 | 0.79 |  | 13 |  |
|  | 8 | CHCC | 13:35 | 9.4 | 95.4 | 10.95 | 0.01 |  | 4 |  |
|  | 9 | UMJC | 14:10 | 9.4 | 121 | 13.9 | 1.09 |  | 30 |  |
|  | 10 | UMSC | 14:20 | 9.3 | 106 | 11.96 | 0.26 |  | 13 |  |
|  | 11 | UM10 |  |  |  |  |  |  |  | NO FLOW |
|  | 12 | GPCC | 15:00 | 9.3 | 104 | 10.95 | 0.31 |  | 8 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | DBCC | 11mg/L |  |  |  |  |  |  |  |  |
| FC | 16BC | 50 |  |  |  |  |  |  |  |  |
| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| 11/9/2004 | 1 | BRFC | 10:30 | 9.2 | 87.2 | 10.05 | 2.3 |  | 500 |  |
|  | 2 | FRFC | 11:40 | 9.4 | 96.0 | 10.98 | 2.03 |  | 80 |  |
|  | 3 | 16BC | 12:20 | 9.8 | 86.1 | 9.75 | 2.85 | 4.55 | 13 | CLEAR-MORNING FOG |
|  | 4 | CEBC | 12:30 | 9.8 | 92.8 | 10.53 | 3.60 |  | 80 | HARD RAIN 11/13/04 |
|  | 5 | DBCC | 13:10 | 9.6 | 44.8 | 5.14 | 1.62 |  | 30 | no chemicals due to holiday |
|  | 6 | CNBR | 12:40 | 11 | 77.3 | 8.54 | 8.92 |  | 130 |  |
|  | 7 | UBCC | 13:15 | 9.4 | 41.9 | 4.79 | 3.32 |  | 30 |  |
|  | 8 | CHCC | 10:00 | 9.2 | 51.4 | 5.92 | 1.55 | 7.55 | 13 |  |
|  | 9 | UMJC | 13:30 | 9.5 | 93.9 | 10.73 | 3.1 |  | 4 |  |
|  | 10 | UMSC | 13:50 | 9.4 | 92.8 | 9.93 | 3.3 |  | 4 |  |
|  | 11 | UM10 | 14:10 | 9.3 | 87.3 | 8.68 | 3.69 |  | <23 |  |
|  | 12 | GPCC | 14:20 | 9.2 | 91.4 | 9.78 | 3.42 |  | 4 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | GPCC | 10mg/L |  |  |  |  |  |  |  |  |
| FC | FRFC | 50 |  |  |  |  |  |  |  |  |

| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 11/22/2004 | 1 | BRFC | 11:00 | 9.3 | 102 | 11.76 | 2.5 |  | 130 | DATE CHANGE FOR HOLIDAY |
|  | 2 | FRFC | 11:20 | 7.8 | 110 | 13.1 | 1.6 |  | 130 | hard rain last week. This am mist to 3pm |
|  | 3 | 16BC | 11:45 | 8.3 | 100 | 11.78 | 2.08 |  | 30 | some clearing-cool apx 45F |
|  | 4 | CEBC | 12:30 | 8.2 | 109 | 12.89 | 2.35 | 4.25 | 30 |  |
|  | 5 | DBCC | 13:10 | 7.8 | 78.4 | 9.45 | 1.85 |  | 30 |  |
|  | 6 | CNBR | 12:50 | 9.4 | 100 | 11.67 | 2.69 |  | 300 |  |
|  | 7 | UBCC | 13:30 | 7.6 | 111 | 13.24 | 4.94 |  | 23 |  |
|  | 8 | CHCC | 12:00 | 7.9 | 78.8 | 9.49 | 1.9 | 7.8 | 30 |  |
|  | 9 | UMJC | 13:50 | 7.6 | 111 | 13.22 | 5.24 |  | 8 |  |
|  | 10 | UMSC | 14:10 | 8 | 110 | 13.06 | 3.81 |  | 8 |  |
|  | 11 | UM10 | 14:25 | 8.7 | 88.9 | 10.35 | 0 |  | 2 | turb rechecked 3 times |
|  | 12 | GPCC | 14:30 | 8 | 110 | 13.13 | 7.05 |  | 4 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | UM10 | 10mg/L |  |  |  |  |  |  |  | spring outlet at Conway Hill Road 4FC/100mL |
| FC | CHCC | 50 |  |  |  |  |  |  |  |  |
| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| 12/20/2004 | 1 | BRFC | 12:00 | 6.8 | 89.8 | 11.14 | 3.53 |  | 900 | DATE CHANGE FOR HOLIDAY |
|  | 2 | FRFC | 11:00 | 6.6 | 101 | 12.4 | 2.92 |  | 23 | hard rain last week--streams have dropped from high |
|  | 3 | 16BC | 12:20 | 6.8 | 92.8 | 11.42 | 3.23 |  | 50 | cool and clear today |
|  | 4 | CEBC | 12:45 | 6.8 | 102 | 12.44 | 3.52 | 4.05 | 50 |  |
|  | 5 | DBCC | 1:10 | 6.8 | 108 | 12.97 | 2.06 |  | 23 |  |
|  | 6 | CNBR | 12:50 | 6.9 | 100 | 11.68 | 2.4 |  | 30 |  |
|  | 7 | UBCC | 1:00 | 6.9 | 99.7 | 9.83 | 2.25 |  | 50 |  |
|  | 8 | CHCC | 10:25 | 6.8 | 75.9 | 9.24 | 1.99 | 8.35 | 8 |  |
|  | 9 | UMJC | 1:35 | 7.1 | 103 | 12.85 | 4.33 |  | <2 | ugly muddy mess |
|  | 10 | UMSC | 1:50 | 7.1 | 100 | 12.12 | 1.52 |  | <2 | pick-up stuck sideways in ditch across road from creek |
|  | 11 | UM10 | 2:00 | 7.6 | 88.7 | 10.62 | 0.01 |  | 4 | salmon carcass at culvert discharge |
|  | 12 | GPCC | 2:05 | 7 | 100 | 12.24 | 4.09 |  | 23 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | 12m/L | 16BC |  |  |  |  |  |  |  |  |
| FC | <2 | UMJC |  |  |  |  |  |  |  |  |
| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| 1/19/2005 | 1 | BRFC | 11:30 | 7.7 | 98.3 | 10.65 | 24.6 |  | 50 | high rains over weekend-entire county under flood |
|  | 2 | FRFC | 11:10 | 7.6 | 99.7 | 11.85 | 22.1 |  | 30 | warning. 16 adult & 1 immature T Swans near CHCC |
|  | 3 | 16BC | 11:30 | 5.1 | 91 | 11.59 | 7.46 |  | 80 |  |
|  | 4 | CEBC | 11:45 | 7.1 | 96.2 | 11.64 | 19.4 | 5.25 | 130 |  |
|  | 5 | DBCC | 1:00 | 8.2 | 84 | 10.07 | 15.2 |  | 130 |  |
|  | 6 | CNBR | 12:00 | 8.6 | 88.2 | 10.28 | 19.5 |  | 80 |  |
|  | 7 | UBCC | 12:15 | 8.9 | 81.3 | 9.76 | 21.2 |  | 50 |  |
|  | 8 | CHCC | 1:15 | 7.8 | 83.3 | 10.06 | 14 | 11.3 | 80 |  |
|  | 9 | UMJC | 1:15 | 7 | 94.3 | 11.48 | 148 |  | 30 | no decimal in turbidity-chocolate brown |
|  | 10 | UMSC | 2:00 | 7.5 | 94.9 | 11.38 | 33 |  | 50 |  |
|  | 11 | UM10 | 2:10 | 7.6 | 94.7 | 11.37 | 31.2 |  | 23 |  |
|  | 12 | GPCC | 2:45 | 7.4 | 94.8 | 11.36 | 29.4 |  | 130 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | 11mg/L | CHCC |  |  |  |  |  |  |  | UMJC FC 30 dupe 130 |
| FC | 130 | UMJC |  |  |  |  |  |  |  |  |

| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2/15/2005 | 1 | BRFC | 11:30AM | 2.9 | 102 | 12.02 |  |  | 80 | COLD AND CLEAR-ICE ALONG STREAM EDGES |
|  | 2 | FRFC | 11:00AM | 2.6 | 104 | 14.13 |  |  | 50 | NO TURBIDITY READINGS TAKEN - USER ERROR |
|  | 3 | 16BC | 11:50AM | 5.2 | 96.7 | 12.27 |  |  | 50 |  |
|  | 4 | CEBC | 12:10PM | 3.4 | 102.0 | 13.59 |  | N/A | 50 | STAFF UNREADABLE-WATER TOO LOW |
|  | 5 | DBCC | 12:35PM | 4.1 | 94.0 | 12.30 |  |  | 30 |  |
|  | 6 | CNBR | 12:20PM | 5.7 | 97.3 | 12.19 |  |  | 4 |  |
|  | 7 | UBCC | 12:50PM | 4.4 | 92.4 | 12.08 |  |  | 30 |  |
|  | 8 | CHCC | 1:15PM | 4.1 | 93.9 | 12.27 |  | 7.65 | 4 |  |
|  | 9 | UMJC | 1:35PM | 2.9 | 102 | 13.80 |  |  | 23 |  |
|  | 10 | UMSC | 1:45PM | 3.4 | 103 | 13.78 |  |  | 13 |  |
|  | 11 | UM10 | 2:00PM | 3.7 | 102 | 13.44 |  |  | 2 |  |
|  | 12 | GPCC | 2:15PM | 3.4 | 103 | 13.55 |  |  | 13 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | 13 | UMSC |  |  |  |  |  |  |  |  |
| FC | 2 | UMSC |  |  |  |  |  |  |  |  |
| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| 3/8/2005 | 1 | BRFC | 11:45AM | 9.4 | 98.3 | 11.25 | 2.59 |  | 13 | Steady rains past 3 days - windy and cool |
|  | 2 | FRFC | 11:15AM | 9.1 | 100.0 | 11.50 | 1.89 |  | 8 |  |
|  | 3 | 16BC | 12:00PM | 9.4 | 98.4 | 11.25 | 1.34 |  | 30 |  |
|  | 4 | CEBC | 12:20PM | ### | 109 | 12.24 | 1.99 |  | 50 |  |
|  | 5 | DBCC | 1:00PM | ### | 89.9 | 10.08 | 1.98 |  | 2 |  |
|  | 6 | CNBR | 12:30PM | 12 | 94.7 | 10.18 | 4.70 |  | <2 |  |
|  | 7 | UBCC | 12:45PM | 9.6 | 98.0 | 11.22 | 2.62 |  | 13 |  |
|  | 8 | CHCC | 1:30PM | 10 | 88.1 | 9.89 | 2.00 |  | 4 |  |
|  | 9 | UMJC | 10:45AM | 10 | 98.7 | 10.69 | 2.37 |  | <2 |  |
|  | 10 | UMSC | 10:30AM | 9.6 | 97.3 | 10.73 | 1.61 |  | 30 |  |
|  | 11 | UM10 | 10:15AM | 9.4 | 97.8 | 11.15 | 1.47 |  | 30 |  |
|  | 12 | GPCC | 10:00AM | 10 | 95.2 | 10.53 | 1.89 |  | 8 |  |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | 10 | DBCC |  |  |  |  |  |  |  |  |
| FC | 2 | UMJC |  |  |  |  |  |  |  |  |
| Date | Site # | Site ID | Time | C | DO % | DO MG/l | Turb | Depth | FC/100mL | Comments |
| 4/12/2005 | 1 | BRFC | 11:10 | 7 | 97.6 | 11.87 | 3.98 |  | 30 | Very wet in pasture-neighbors horses got in past 3 months |
|  | 2 | FRFC | 10:35 | 7 | 104.4 | 12.6 | 5.21 |  | 50 | No Rick-arrived too early-next time at 10:50 |
|  | 3 | 16BC | 11:45 | 8.9 | 99.6 | 14.49 | 2.2 |  | 13 |  |
|  | 4 | CEBC | 11:50 | 7.8 | 107 | 12.67 | 5.04 | 4.55 | 80 |  |
|  | 5 | DBCC | 12:10 | 8.1 | 93.9 | 11.03 | 6.1 |  | 130 | Water dropped apx 3-4 inches at alder instream this site |
|  | 6 | CNBR | 12:00 | 9.2 | 101 | 11.53 | 5.23 |  | 30 |  |
|  | 7 | UBCC | 12:20 | 8.1 | 91 | 10.75 | 18.2 |  | 50 | Bacteria / algae visible in water sample |
|  | 8 | CHCC | 10:05 | 7.8 | 99.5 | 11.84 | 6.77 |  | 50 | Nearly bankfull |
|  | 9 | UMJC | 9:45 | 6.7 | 87.5 | 10.71 | 4.79 |  | 13 | Bacteria bubbles |
|  | 10 | UMSC | 9:35 | 6.6 | 97.1 | 11.8 | 5.15 |  | 13 | Ephemeral active RB downstream of sampling site |
|  | 11 | UM10 | 9:25 | 6.8 | 74.8 | 9.22 | 0.42 |  | 13 |  |
|  | 12 | GPCC | 9:30 | ### | 97.1 | 11.95 | 10.82 |  | 50 | Nearly bankfull--high velocity flow |
| Dupes |  |  |  |  |  |  |  |  |  |  |
| Winkler | 12 | 16BC |  |  |  |  |  |  |  | hard rains over weekend into Monday-hard hail Monday |
| FC | 30 | FRFC |  |  |  |  |  |  |  | cloudy and cool today--brisk wind--rainy off and on |

Appendix 5- Endangered Species

LISTED AND PROPOSED ENDANGERED AND THREATENED SPECIES AND CRITICAL HABITAT; CANDIDATE SPECIES; AND SPECIES OF CONCERN

IN WESTERN WASHINGTON

AS PREPARED BY

THE U.S. FISH AND WILDLIFE SERVICE

WESTERN WASHINGTON FISH AND WILDLIFE OFFICE

(Revised December 20, 2005)

SKAGIT COUNTY

LISTED

Wintering bald eagles (Haliaeetus leucocephalus) occur in the county from about October 31 through March 31.

There are 25 bald eagle communal winter night roosts located in the county.

There are 11 bald eagle wintering concentrations located in the county in the following areas: Fidalgo Island; Guemes Island; Skagit River-S. Fork Nooksack River; Skagit River; Skagit-Sauk Rivers; Corkindale Staging Area; Illabot Creek Staging Areas; and Samish Bay.

There are 77 bald eagle nesting territories located in the county. Nesting activities occur from about January 1 through August 15.

Bull trout (Salvelinus confluentus) occur in the county.

Canada lynx (Lynx canadensis) may occur in the county.

Gray wolves (Canis lupus) may occur in the county.

Grizzly bears (Ursus arctos = U. a. horribilis) may occur in the county.

Marbled murrelets (Brachyramphus marmoratus) occur in the county. Nesting murrelets occur from April 1 through September 15.

Northern spotted owls (Strix occidentalis caurina) occur in the county throughout the year.

Major concerns that should be addressed in your Biological Assessment of project impacts to listed species include:

1.         Level of use of the project area by listed species.

2.         Effect of the project on listed species' primary food stocks, prey species, and foraging areas in all areas influenced by the project.

3.         Impacts from project activities and implementation (e.g., increased noise levels, increased human activity and/or access, loss or 
degradation of habitat) that may result in disturbance to listed species and/or their avoidance of the project area.

Castilleja levisecta (golden paintbrush) may occur in the county.

Major concerns that should be addressed in your Biological Assessment for this listed plant species include:

1.         Distribution of taxon in project vicinity.

2.         Disturbance (trampling, uprooting, collecting, etc.) of individual plants and habitat loss.

- Changes in hydrology where taxon is found.

DESIGNATED

Critical habitat for the northern spotted owl has been designated in Skagit County.

Critical habitat for the marbled murrelet has been designated in Skagit County.

Critical habitat for the bull trout has been designated in Skagit County.

PROPOSED

None

CANDIDATE

Fisher (Martes pennanti) (West Coast distinct population segment)

Oregon spotted frog (Rana pretiosa)

SPECIES OF CONCERN

California wolverine (Gulo gulo luteus)

Cascades frog (Rana cascadae)

Long-eared myotis (Myotis evotis)

Long-legged myotis (Myotis volans)

Northern goshawk (Accipiter gentilis)

Olive-sided flycatcher (Contopus cooperi)

Pacific lamprey (Lampetra tridentata)

Pacific Townsend’s big-eared bat (Corynorhinus townsendii townsendii)

Peregrine falcon (Falco peregrinus)

River lamprey (Lampetra ayresi)

Tailed frog (Ascaphus truei)

Western toad (Bufo boreas)